## Slide 1: UVM Register Map Dynamic Configuration
Matteo Barbati, STMicroelectronics
Alberto Allara, STMicroelectronics

## Slide 2: Outline
Motivation
UVM Register Model
Case Study
Custom Code Example
IP-XACT Example
Proposed Approach
Real Case Example
PROs and CONs
Conclusion & Future Works

## Slide 3: Motivation
Automatize the synchronization of the UVM register model with any verification component in the environment
Reduce the usage of ad-hoc solutions that are error prone

## Slide 4: UVM Register Model
Memory—uvm_mem
Address Map - uvm_reg_map
UVM Register Model
Register Block—uvm_reg_block
...
R1
R2
R3
RN
F1
F2
F3
F4
F5
FN
Registers—uvm_reg
Fields—uvm_reg_field

## Slide 5: Case Study
Scenario
  Create a verification environment that dynamically change behavior according to the configuration of a register.
    For instance consider register called “MODE”
  Generate an event every time the fields of our case study register are written
State of the Art
  Custom Code
  IP-XACT

## Slide 6: Custom Code Example
Extend “MODE_type” class
  Adding logic to correctly manage UVM events
  class trig_MODE_type extends MODE_type;
    …
    uvm_event_pool ep;
    uvm_event e;
    string event_name = "mode_type_e";
    …

## Slide 7: Custom Code Example (2)
  Generating event at each write operation
      virtual task post_write(uvm_reg_item rw);
      `uvm_info("trig_MODE_type", "**** Firing Write trigger ****", UVM_HIGH);
      e.trigger();
      endtask: post_write
      Endclass
Overwrite the original class in the environment
    …
    set_type_override_by_type(MODE_type::get_type(),
    trig_MODE_type::get_type());
    …

## Slide 8: IP-XACT example
Customize IP-XACT regmap description
<vendorExtensions:description>My post_write </vendorExtensions:description>
<vendorExtensions:code>
virtual task post_write(uvm_reg_item rw);
uvm_event_pool ep;
uvm_event e;
`uvm_info("trig_MODE_type","**Firing Write trigger**",UVM_HIGH);
ep=uvm_event_pool::get_global_pool();
e = ep.get("mode_type_e");
e.trigger();
endtask: post_write
</vendorExtensions:code>

## Slide 9: IP-XACT Example (2)
Run the UVM register map generation flow
    …
    virtual task post_write(uvm_reg_item rw);
    uvm_event_pool ep;
    uvm_event e;
    `uvm_info("trig_MODE_type", "** Firing Write trigger **", UVM_HIGH);
    ep = uvm_event_pool::get_global_pool();
    e = ep.get(event_name);
    e.trigger();
    endtask: post_write
    …

## Slide 10: Proposed Approach
Overview
  Modify uvm_reg_field adding logic to generate triggers
  Substitute uvm_reg_field with the new one
Implementation
  Modify pre_read and pre_write to manage configuration through uvm_config_db
  Add a lazy initialization mechanism
  Modify pre_read, pre_write, post_read and post_write to trigger events

## Slide 11: Proposed Approach (2)
New uvm_reg_field class
  Add required uvm events and support variables
    uvm_event_pool ep;
    uvm_event pre_rd_e, pre_wr_e, post_rd_e, post_wr_e;
    local string pre_rd_event_name; local string pre_wr_event_name;
    local string post_rd_event_name; local string post_wr_event_name;
    local bit en_pre_rd_event, en_pre_wr_event, en_post_rd_event, en_post_wr_event;
    …
    local bit conf;

## Slide 12: Proposed Approach (3)
New uvm_reg_field class
  Implement configuration mechanism
    virtual task pre_read(uvm_reg_item rw);
    if(conf) begin
    uvm_config_db#(bit)::get(uvm_root::get(), get_full_name(), "en_pre_rd_event", en_pre_rd_event);
    uvm_config_db#(bit)::get(uvm_root::get(), get_full_name(), "en_pre_wr_event", en_pre_wr_event);
    uvm_config_db#(bit)::get(uvm_root::get(), get_full_name(), "en_post_rd_event", en_post_rd_event);
    uvm_config_db#(bit)::get(uvm_root::get(), get_full_name(), "en_post_wr_event", en_post_wr_event);
    conf = 1'b0;
    end
    …
    endtask : pre_read

## Slide 13: Proposed Approach (4)
New uvm_reg_field class
  Customize callbacks to generate event if required
    virtual task pre_read(uvm_reg_item rw);
    …
    if(en_pre_rd_event) begin
    `uvm_info(get_name(), "**** Firing Pre Read trigger ****", UVM_HIGH)
    pre_rd_e.trigger();
    end
    endtask : pre_read
    virtual task post_read(uvm_reg_item rw);
    if(en_post_rd_event) begin
    `uvm_info(get_name(), "**** Firing Post Read trigger ****", UVM_HIGH)
    post_rd_e.trigger();
    end
    endtask : post_read

## Slide 14: Proposed Approach (5)
Replace uvm_reg_field class with the new class in the environment
Turn on event generation for the desired fields
    …
    set_type_override_by_type(uvm_reg_field::get_type(),uvm_reg_field_ext::get_type());
    uvm_config_db#(bit)::set(uvm_root::get(), "regmap.MODE.field1", "en_post_wr_event", 1);
    uvm_config_db#(bit)::set(uvm_root::get(), "regmap.MODE.field3", "en_post_wr_event", 1);
    uvm_config_db#(bit)::set(uvm_root::get(), "regmap.MODE.field4", "en_post_wr_event", 1);

## Slide 15: Real Case Example
Test_1
…
Write_field(tx_data_witdh, 32);
Register
Model
TX VIP Master
Agent
RX VIP Slave
Agent
RX VIP Master
Agent
TX VIP Slave
Agent
Tx Datapath
Rx Datapath
Tx Scoreboard
Rx Scoreboard
postwr_tx_data_width
tx_data_width = 32
...
uvm_config_db#(bit)::set(uvm_root::get(), "register_model.reg1.tx_data_width", "en_post_wr_event", 1);
1
2
3
4
5
5
5
APB VIP
Master
APB

## Slide 16: PROs & CONs
 | Custom Code | IP-XACT flow | Proposed Approach
Pros | Code optimized: events generated only where needed | Code optimized: events generated only where needed | More flexibility: Event generation can be dynamically configured Reduce code impact in case of customization needed on high number of registers
Cons | Error prone in case of high number of registers to customize | Error prone in case of high number of registers to customize Need to rerun the entire flow in case of changes in register customization Different version of the same IP-XACT description. One for Design and one for Verification | Size Overhead affecting all the fields of the entire register map 9 extra variables 4 extra uvm events

## Slide 17: Conclusions & Future Works
Reduced error prone approach
To reduce impact related to Data Size Overhead
  “cluster of events”

## Slide 18: Questions