## Slide 1: Using High-level Synthesis and Emulation to Rapidly Develop AI Algorithms in Hardware
John Stickley – Emulation Technologist
Petri Solanti – Field Application Engineer, HLS

## Slide 2: Computer Vision/AI Application Challenges Automotive and other “real-time” applications especially challenging
Continually changing algorithms and sensors
Computationally very expensive
  Billions of operations/second
High responsiveness required
  High-bandwidth and low-latency
  Real-time processing of data required
Autonomous drive - solution required to be < 100w
Each provider wants to add their “secret sauce”
ADAS and Driverless Cars
Notes: Introduce the challenges that are faced by not only Tier1’s but OEM’s as they want to design their own SW and eventually HW for autonomous driving. They don’t like the solutions that are out there because they do not meet all of these criteria
Just like any modern algorithm to hardware design, computer vision/AI algorithm to hardware design is becoming more and more challenging. This is because of the continuous evolution of both the algorithms, sensors, and display technologies. Implementations of these algorithms in hardware is already computationally very expensive, requiring many billions of computations per second. This computational complexity will only continue to grow as sensor and camera resolutions are expected to double every couple of years. This doubling of computational requirements will make it even harder to deliver new IP on time or to roll late stage algorithmic changes into the latest products.
The real-time responsiveness requirements needed for implementing high-bandwidth, low latency, hardware means these systems require massive parallelism, making low power extremely important.

## Slide 3: Convolutional Neural Networks: Training vs Inferencing (Embedded AI)
Very large datasets and memory, CPU/GPU farms, floating point required
Uses data from trained network, end system often has real-time requirements, can go to FPGA/ASIC and dedicated HW, can be reduced to fixed point, can implement low-power
Catapult High-level Synthesis (HLS) fits here
Notes: There are two parts to developing Convolutional Neural Networks (CNNs).
The training stage requires very large datasets, massive amounts of memory storage, floating point, and days of computation time on a GPU farm. Training involves feeding the network input training data and looking at the output for the desired classification. And error is computed at the output between the expected result and the actual result and is used for a back propagation calculation of new weights. This is very similar to the gradient descent algorithms used in adaptive filtering to calculate coefficient fort channel equalization.
The inference engine is a feed-forward network that uses the weight from training to classify an input image. This is often run in real-time, can be fixed point, and power is important.

## Slide 4: Next-generation Computer Vision Designs Require Much More Parallelism
Convolutional Neural Networks use lots of 2-d convolutional filters
  Lots of multiply-accumulate math
Multiple convolutional layers
Networks are constant evolving
  Data rates, number of layers, image size, etc..
16 2-d convolutional filters
36x16 = 576 2-d convolutional filters
Simple 2-layer CNN for Character Recognition
Feature maps
Fully connected layer uses matrix multiplication
Notes: Next generation computer vision design using Convolutional Neural Networks (CNNs) require massive amounts of parallelism to run in real-time. Classic computer vision/image processing hardware may have a few convolutional filters, but this is insignificant compared to CNNs.
CNNs are essentially algorithms that can perform object detection and classification. The CNN is made up of multiple layers, where each layer performs multiple sets of convolutions. Each layer has a set of input channels and output channels, which are also referred to as feature maps. The convolutional filters for each layer are essentially “feature detectors” that are programmed to look for certain characteristics such as horizontal lines, vertical lines, etc. It is common for the number of input and output channels to double as you progress through the layers, which results in the explosion in the number of convolutional filters as well as the filter weights (coefficients). You can see in the simple CNN diagram shown about that the first layer has 1 input channel and 16 output channels and requires 16 different convolutional filter kernels. The second layer has 16 input channels and 36 output channels requiring 36x16 = 576 2-d convolutional filters. In many CNNs the last layer(s) consist of fully connected layers which are usually implemented using matrix multiplication.
Key takeaways:
CNNs are doing object detection and classification
Massive computational complexity
Number of filters can get huge the deeper you go into the layers
Potentially tens of millions of weights will have to be stored somewhere. Not pratical to keep all on chip.

## Slide 5: Acceleration of the Architectural Exploration Design Phase
HLS-synthesized CNN-based machine learning algorithms lend themselves favorably to take advantage of a highly parallel simulation engine such as an emulator
  The speed of execution of simulating the design on an emulator does not change with the addition of more layers to the CNN algorithm
  Whereas with software simulation, performance goes down roughly linearly with migration of each layer to RTL
Notes: RTL simulation can take hours to simulate a single frame of even a simple CNN like yolo tiny. This makes evaluating real time behavior of multiple frames (30 fps) painfull.

## Slide 6: What are the Choices for Hardware Platform? There is no clear winner today as this market is emerging
CPU
  Not fast or efficient enough
DSP
  Good at image processing but not enough performance for Deep AI
GPU
  Good at training but too power hungry for long term inferencing solution
FPGA
  Low-power, mostly meets performance/latency, RTL flow not practical, not the lowest power, eventually cost for volume a problem
ASIC
  Lowest power, meets performance/latency, high NRE and no field modifications/upgrades, Algorithms still changing, RTL flow not practical, lowest volume cost
Dedicated AI and CV processors or accelerators in IP and ASIC
  Popping up like weeds – high performance, locks customer in, many server target
Some scalable combination of the above
Flexibility
Power
Notes: Today there is no clear solution for implementing CNNs but as the market matures custom ASIC will be required for both power and cost.
GPUs are the clear winner for training CNN networks today but are costly in terms of power consumption as well as area. They are not practical for implementing an inference engine for large scale production.
FPGAs are a lower-power solution compared to GPUs and have the advantage of re-programmablity but also have several drawbacks.
Hand-coding RTL is not practical for next-generation computer vision algorithms
Low power, but not compared to ASIC
Volume cost is expensive
ASIC is the lowest power, lowest latency, solution with the lowest volume cost. However it does not have the flexibility of FPGA as the architecture is fixed. Although the CNN algorithms are still evolving there will be a need to go to ASIC. Going to ASIC will have the challenge of delivering new and complex designs on time, where manual RTL creation is no longer pratical.

## Slide 7: Numerous Possible Hardware/Memory CNN Architectures
Notes: There are many possible hardware and memory architectures for CNNs. A Google search will return hundreds of papers on the different ways CNNs can be implemented. Every implementation is trying to solve a specific problems such as minimizing area, power, or memory bus traffic. Depending on the target application there is no one size fit’s all solution. How can a designer know what is the best architecture for their custom application? When hand-coding RTL it is not possible to explore more than one or two architectures.

## Slide 8: Memory Architecture and Power Considerations
Keeping data local is key to minimizing power consumption
  Very important for ASIC
Floating-point is costly
  Used in training of networks
  Not needed in network inference engine
Fixed-point doesn't need to be power-of-two
*NVIDIA 2017
Notes: Along with all of the possible architectures, power is a big consideration. Modern CNN’s have tens of millions of weights. It is not practical to store these weights locally because of the cost of on-chip memory. This means read the weights from system memory (DRAM). The figures show above came from an NVIDIA paper on the cost of reading data from off-chip. They demonstrated that reading data from system memory has 200/6=33x more energy consumption than reading from local memory, and 200x the cost from keeping data in registers.
Additionally, 32-bit floating point is expensive. While it is used in the training of the network, it is not needed in the inference engine implementation. Furthermore fixed-pint implementations do not need to be power-of-two bits, The figure, bottom-right, shows the difference if energy cost between 32, 16, and 8 bits. HLS is not restricted to this coarse-grained bit width.

## Slide 9: Catapult HLS is the Only Solution for Rapid Algorithm to RTL
Enable late functional changes without impacting schedule
  Algorithms can be easily modified and regenerated
  New technology nodes are easy (or FPGA to ASIC)
Quickly evaluate power and performance of algorithms
  Rapidly explore multiple options for optimal Power Performance Area (PPA)
Accelerate design time with higher level of abstraction
  1 Year reduced to a few months
  New features added in days not weeks
  5X less code than RTL
void func (short a[N],
for (int i=0; i<N; i++) {
if (cond)
z+=a[i]*b[i];
else
RTL

## Slide 10: Why Catapult HLS is So Much More Productive than RTL
Catapult HLS separates functionality from implementation with powerful tool capabilities for controlling implementation
Catapult Implementation Control
Automatically
  Builds concurrent RTL from C++ Classes or Functions
  Adds Interfaces
  Closes Timing
  Memory inferencing and constraints for architecture
  Resource sharing for minimal area
  Constraints drive parallelism - Unrolling
Functionality Described in C++ or SystemC
+
RTL
Using High-level Synthesis and Emulation to Rapidly Develop AI Algorithms in Hardware
10

## Slide 11: Precise Modeling of Bit-accuracy
HLS uses exact bit-widths to meet specification and save power/area
  bit-widths are not always pow2 (1, 8, 16, 32, 64 bits)
Rapid simulation of true hardware behavior
RTL is correct by construction
  Precise consistency of representation and simulation results between C++ algorithm and synthesized RTL
C++/SystemC using bit
accurate integer/fixed-point
Measure/Verify
Refine/Explore
Precision
Model
using floating-point
Bit-accurate RTL
Catapult Ultra
Verify
The Algorithmic C fixed point data types are declared as:
ac_fixed<W,I,S> x;
width
#integer bits
Notes: HLS allows us to model the true hardware behavior using arbitrary precision bit-accurate data types. This not only allows rapid simulation of the hardware in C++, but also provides correct-by-construction RTL that is a bit-for-bit match with the C++ making verification easy, and likely to pass the very first time. It also provides a way to easily co-simulate and debug against the golden reference model which can be a floating point model and is written in C++.

## Slide 12: RTL Creation and Verification is Still a Bottleneck
Going from AI development platform to optimized RTL is not well understood
  How to verify hardware implementation
  How to quantize and optimize the HW
HLS delivers optimized RTL quickly but…
  RTL verification is slow
  Hours/days/weeks of simulation on complex CNN designs
AI Development Platforms
HDL Simulator
Stimulus
RTL
code
coverage goal reached?
no
Add tests
Done
UCDB
Coverage
Exclude Unreachables
Questa
CoverCheck
?
Quantization
Architectural optimization
RTL verification
Notes: Creating and verify RTL designs that implement CNNs is difficult today.
The AI platforms (Tensorflow, Caffe, pytorch, etc) are not well understood.
  They only target CPU and GPU
  They are only in 32-bit float
  There is no easy way to get from the AI platform to an RTL implementation and verify it. This includes quatization of the floating point algorithm
HLS already provides a way to quickly get to RTL but:
  How to verify against the original floating point CNN
  RTL verification is extremely slow. We may need to verify 30 frames/sec multiple seconds of video to test things like pedestrian detection for autonomous driving. This is days of RTL simulation.

## Slide 13: Catapult and Veloce Solve the Verification Bottleneck
Quickly verify synthesizable HLS C++ and RTL in the Tensorflow environment
  Test the quantized HLS against the floating point model in tensorflow
Reduce RTL verification from hours to minutes
AI Development Platform
HLS Model in C++
Catapult HLS
Optimized RTL
Synthesized RTL model module yolo_tiny(…)
XlAcChannelMaster (driver+xactor)
XlAcChannelSlave (driver+xactor)
Tensorflow Operator API Wrapper
Driver “proxy”
C++ model yolo_tiny.run(…)
Veloce
Notes: Catapult can leverage the Tensorflow Operator API to generate a C++ wrapper (currently not automated) that allows the synthesizable fixed-point C++ to be run inside of tensorflow allowing the tensorflow test bench to be reused to verify if the fixed-point synthesizable model is correct. The API wrapper takes the Tensors (which are just arrays with one or more dimensions) from tensorflow and writes them into ac_channels that drive the HLS DUT.
This same C++ API wrapper is where the Veloce hardware transactors are inserted that allow the tensorflow stimulus to be intercepted and driven to the Veloce emulator. These same transactors will also convert the pin-level data coming back from Veloce into C++ transactions which are then converted back into Tensors and set back to the tensorflow.

## Slide 14: Even “Small” CNNs are Computationally Intensive
Yolo Tiny*
  used in object detection and classification for cell phones
  Over 70 Billion MAC/Sec
  Over 25 million weights
Made up of mostly 2-d convolution and pooling layers
* Courtesy of Joseph Redmon, https://pjreddie.com/darknet/yolo
Notes: The Yolo Tiny CNN, which stands for You Only Look Once” is a CNN that will do object detection and classification in a single pass. It detects 20 different objects from people to cars, etc. Even though this is considered a small CNN it still requires massive amounts of computation and has over 25 million weights.
Notes added by johnS
Pooling layers between convolutional layers serve to spacially downsample the data which is required to keep feature maps of reasonable size
  Also to allow subsequent convolution layers to be cognizant of inputs with increasingly greater separation

## Slide 15: Yolo Tiny* progressive refinement
This “Yolo Tiny” demo is based on the Google TensorFlow open-source machine learning technology based in Python
The intent of the demo is to show techniques for progressive refinement from high-level abstracted TensorFlow CNN layer models written in Python3 down to HLS-synthesized RTL, i.e.,
    Original TensorFlow code HLS “synthesis-friendly” C++ blocks Synthesized RTL blocks
  Then re-validation after each refinement, ultimately deploying an emulator for validation of synthesized RTL blocks
* Courtesy of Joseph Redmon, https://pjreddie.com/darknet/yolo

## Slide 16: Architectural exploration acceleration and early tradeoff analysis
Specifically we're exploring an approach that still keeps the whole flow in the architectural exploration phase of a machine learning design project, even while playing with the software/hardware representational tradeoffs
  And, because emulation is deployed, being able to accelerate the RTL verification as well as starting to look at early power analysis, performance, etc.
All of this can potentially be done before even thinking about bringing interface synthesis into the picture and targeting real hardware bus interfaces
  I.e. doing all architectural exploration - even at RTL abstraction while using strictly abstract bit accurate native HLS data types such as ac_fixed<>, ac_channel<>'s for communication, etc.

## Slide 17: YoloTiny: Original python3/TensorFlow testbench
conv2d
conv2d
conv2d
conv2d
conv2d
conv2d
conv2d
conv2d
conv2d
maxpool
maxpool
maxpool
maxpool
maxpool
maxpool
stage
layer
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
input tensor
x
output tensor
o9
9 stage CNN with 9 conv2d layers the first 6 of which are separated by maxpool layers which then feed densely connected conv2d layers
First conv2d layer is fed an input tensor ‘x’ which is the 2-dimensional preprocessed_image from the top level python3 test.py testbench
9th stage provides recognized images in the output tensor ‘o9’ which is fed back up to top the level test.py for post processing of the output image, with classification and bounding box info included
Each conv2d image is fed learned weights and biases for that stage
Where preceded by a maxpool layer, it is fed by the output of that layer, otherwise simply the output of the preceding conv2d layer
TensorFlow testbench

## Slide 18: Quickly Implement CNN Architectures Using HLS
Easily code multiple architectures in C++
  Sliding-window architecture processes fmap data in raster order
  In-place architecture reads weights once
HLS constraints allow architectural exploration
  Massive parallelism is possible
  Evaluate power, performance, and area PPA across multiple architectures and microarchitectures
Sliding-Window
Convolution / Max Pooling
Sliding-Window
Convolution/ Max Pooling
FIFO
Sliding-Window
Convolution/ Max Pooling
….
FIFO
In-place
Convolution/ Max Pooling
Off-chip DRAM
AXI4 stream
Weights and results
FMAP_HEIGHT:for(int r=0;r<IN_HEIGHT;r++){
IN_CHAN:for(int ic=0;ic<IN_CHANNELS;ic++){
FMAP_WIDTH:for(int c=0;c<IN_WIDTH+1;c++){
< Read feature map data stream >
< Sliding window of feature map data >
OUT_CHAN:for(int oc=0;oc<OUT_CHANNELS;oc++){
< Read kernel weights from SRAM >
KERNEL_Y:for(int i=0;i<3;i++){
KERNEL_X:for(int j=0;j<3;j++){
acc += fmap_window[r+i][c+j] * kernel[i*3+j];
}
}
< Write out partial output channel sums >
}
}
}
}
Loops can be unrolled
36-parallel multipliers
YOLO Tiny
Notes: HLS allows designers to quickly implement and explore different architectural solutions using C++ as the design language. The implantation that was chosen was based on the design requirement that the weights would only be read once from system memory to minimize power consumption. This required using a “dual-layer” architecture where the earlier layers used a “sliding-window” architecture to minimize re-reading the input channel data, and the later layers used an in-place architecture to only read the weights once from DRAM. Each one of these layers was tuned for performance using high-level synthesis constraints such as loop unrolling to add parallelism in order to perform multiple computations in paralle.

## Slide 19: Easily Test HW Models and RTL Quickly
Swap any layer or the entire design
  HLS C++ executable or RTL running on Veloce is a python function call in tensorflow
catapult
conv2d
Sliding-Window
Convolution/ Max Pooling
FIFO
Sliding-Window
Convolution/ Max Pooling
….
FIFO
In-place
Convolution/ Max Pooling
Off-chip DRAM
AXI4 stream
Weights and results
Tensorflow Python File
Tensorflow Operator wrapper call
Veloce
Tensorflow C++ API Operator Wrapper
Veloce Driver
Optimized RTL
HLS Model in C++
Notes: The Yolo Tiny tensorflow model was used as the starting point. This model is written in python and consists of a number of python function calls to implement the different layers of the CNN. The python function calls implement things like 2-d convolution, max pooling, etc. As the HLS code was developed for each layer the python function call was “swapped” out with the HLS model and then the tensorflow testbench was re-run to verify that the HLS C++ implementation did not break the CNN. Once the HLS mode was verified it was synthesized in Catapult and the synthesized RTL was run on Veloce which sent the RTL output back to the tensorflow via the Velcoe transactors and tensorflow API, again verifying that the RTL was correct.

## Slide 20: YoloTiny: Selected layers of TensorFlow testbench broken out to “HLS-friendly” C++ implementation-targeted algorithms
conv2d
conv2d
conv2d
conv2d
conv2d
conv2d
conv2d
conv2d
maxpool
maxpool
maxpool
maxpool
maxpool
TensorFlow testbench
stage
layer
1
2
3
4
5
6
7
8
9
3
4
5
6
7
8
9
10
11
12
13
14
15
input tensor
x
output tensor
o9
conv2dHls
1
2
layer
maxpoolHls
stage
1
HLS C++ code block
input tensor
x
output tensor
o9
TensorFlow testbench
1-stage breakout
Pre-processing of data input, weights, biases
Assembling inputs into AcChannel stream to feed synthesizeable algorithm
HLS C++ code block
Pre-processing
Synthesizeable hardware implementation-targeted 9-stage CNN algorithm
9-stage CNN
Post-processing of data output from AcChannel stream
Re-format to go back to Tensorflow testbench
Post-processing
9-stage breakout
Here we break out 1 or more of the original TensorFlow layers to experiment with implementation synthesis
We still run the new C++ code prototypes in the context of the original TensorFlow testbench
We pre-verify the synthesizeable code even before we generate RTL from it

## Slide 21: Easy Modeling, Synthesis, and Emulation of Streaming Interfaces
AC channel parametrized class allows designers to model streaming data interfaces in untimed C++
Easily map ac_channel<> to emulator transactor API, XlAcChannel*Driver for software/hardware communication
  C++ testbench drives stimulus to emulator
data_in 0
data_in 1
data_in 2
data_in N
Emulator Proxy
XlAcChannel
*Driver
C++ Testbench
ac_channel
Read from channel
Channel data types
Stream to driver instead
HLS synthesizeable block
Emulator ac channel driver API
Notes: Real hardware often sends and receives sample data in a streaming fashion. This must be modeled in the source and in the past using pointers proved to be risky and error prone. The ac_channel class was designed to allow efficient modeling of streaming interfaces. ac_channel allows a streaming producer/consumer behavior to be enforced resulting in correct by construction RTL. In software ac_channel behaves like an infinite FIFO and is used on the top-level interface as well as to interconnect different blocks in a sub-system.
The ac_channel interface can be easily mapped to the emulator transactor and driver allowing the C++ testbench to drive the stimulus to the emulator.

## Slide 22: Interface Synthesis Makes HW Communication with Veloce Easy
Veloce
XlAcChannel
*Driver
Interface synthesis allows the interface protocol to be defined using the HLS tool
ac_channel maps to data/ready/valid protocol in hardware (*_wait interface)
XlAcChannel*Transactor and *_wait interfaces bolt together seamlessly
Catapult Architectural Constraints View
C++ Testbench
XlAcChannel*Transactor
Catapult
RTL
*_wait Interface
ac_channel
Notes: Only the port size and direction are inferred from an untimed C++ function interface. Interface synthesis allows the port protocol to be defined in the HLS tool. The most typical protocols are point-to-point protocols with request/acknowledge type handshake behavior, or memory interfaces for larger arrays. You can see in the example above that the C++ source contains no explicit protocols for the interfaces but can result in a handshaking interface.
Catapult’s knowledge of how ac_channel interfaces are synthesized can allow us to easily automated the flow, similar to SCVerify, where the DUT function call is intercepted and replaced to calls to the emulator transactor and drivers.

## Slide 23: YoloTiny: C++ implementations of CNNs replaced with synthesized RTL blocks
conv2d
conv2d
conv2d
conv2d
conv2d
conv2d
conv2d
conv2d
maxpool
maxpool
maxpool
maxpool
maxpool
TensorFlow testbench
stage
layer
1
2
3
4
5
6
7
8
9
3
4
5
6
7
8
9
10
11
12
13
14
15
input tensor
x
output tensor
o9
stage
1
HLS C++ code block
input tensor
x
output tensor
o9
TensorFlow testbench
1-stage breakout
Pre-processing of data input, weights, biases
Assembling inputs into AcChannel stream to feed synthesizeable algorithm
HLS C++ code block
Pre-processing
C++ driver “proxy” model
9-stage CNN
Post-processing of data output from AcChannel stream
Re-format to go back to Tensorflow testbench
Post-processing
9-stage breakout
Here we replace each of the C++ algorithm breakouts shown previously with actual RTL code running on the emulator
The C++ blocks themselves become AcChannel drivers to AcChannel BFMs running in the emulator
All of this is still running in the context of the original python3/TensorFlow testbench
Cross-process TLM based XlAcChannelDrivers couple the TensorFlow and HLS C++ remote client process with the co-model host process and the emulator
Catapult synthesized conv2dHls RTL model
XlAcChannel* (drivers+xactors)
Emulator
C++ driver “proxy” model
Catapult synthesized 9 stage CNN RTL model
Emulator
XlAcChannel* (drivers+xactors)

## Slide 24: Memory Inference and 0-time Back-Door Memory Accesses
Large C++ arrays automatically mapped to ASIC or FPGA memories
Well supported in emulation using general purpose XlMemoryTransactor module
Arrays on the design interface can be synthesized as memory interfaces
Internal arrays synthesized to instantiated (black boxed) memories
Sythesized RTL
XlMemoryTransactor
(open-kit)
Memory interface protocol
Instantiated memory transactor with 0-time back-door interface
Catapult Architectural Constraints View
Notes: Interface synthesis allows Catapult to map a C++ array on the design interface to a memory interface that consists of address, data, and control signals. These 0-time C++ memory transactions will directly map to the emulator memory transactor allowing easy testing of memory interfaces on the generated RTL. Additionally, Catapult will infer large internal arrays to instantiated memories in the RTL, which can be synthesized directly by Veloce.

## Slide 25: Some Customer testimonial examples

## Slide 26: NVIDIA Cuts Verification Cost by 80%
10M gates video decoder for Tegra X1
Schedule and goals couldn’t be met without adding 20 engineers to a team of already 60
Invested in Catapult instead
  Improved design productivity by 50%
  Cut verification cost by 80%
“Saved their skin – Twice”
  Converted VP9/H.265 from 8 to 10 bit color in weeks
  Re-optimized IP from 20nm/500Mhz to 28nm/800Mhz in 3 days
Traditional RTL
Full Regression
3 months
1000 CPUs
Time
Resources
Time
HLS C++
Full Regression
2 weeks
14 CPUs
Resources
Source: NVIDIA white paper
http://go.mentor.com/4N9cP

## Slide 27: NVIDIA Research New Methodology with Catapult Machine Learning Accelerator SoC using an Object-Oriented HLS flow
NVIDIA Research with DARPA - New methodology for 10x faster chip design
Developing libraries of HLS components to target 80% of future NVIDIA chips
Used in NVDLA HW
2 DAC Papers; 2016,2018
Hardware Accelerator for Mobile Computer Vision Applications
Digital VLSI Flow for High-Productivity SoC Design
Notes: New presentation “Design and Verification of a Machine Learning Accelerator SoC using an Object-Oriented HLS-based design flow”

## Slide 28: Bosch Automotive Catapult Success
Bosch needed big change to stay #1 in Automotive Safety
Started new subsidiary for Autonomous Driving
Decided HLS * lack of resources *quickly react to changes
Mentor worked as key partner with a focus on success
Result - Catapult HLS success on time first IP deliverable
Delivered new designs ahead of schedule in 7 months with evolving specifications; improved quality over RTL
BOSCH VISIONTEC Rapidly Brings New Automotive IP to Market using Catapult HLS Platform
Notes: Automotive Safety market is shifting to automated cars
  In order for Bosch to keep its #1 position must completely change their “communication with the outside”
Realized they did not have the expertise especially for image processing – Opened a new subsidiary for pure digital design, start business from scratch – Bosch Vision Tech – Sophia Antipolis and hired some ST folks
Decided HLS and did an evaluation which surprised them that we won because Cadence has an office right there.
Did not have enough resources –
Stakes were high so needed a business model to help guarantee their success - Partner with consulting delivered both a designer & knowledge transfer HLS
Some IP’s HLS, Some IP’s hand-coded RTL
So successful with HLS 3 IP’s originally(delivered on-time) that they took on RTL IP’s that were late from other groups (2 IP’s by themselves with no help because they were very secret)
Very happy champion customer, joint white paper, etc.
We are now also doing ISO26262

## Slide 29: ST Imaging HLS Success for ISP (Automotive)
To date created 50+ Image Processing IPs using HLS Imaging Template
Why they use HLS and Catapult (their words)
  Increase IP value
  Improve IP performance versus power & area
  Reduce project cost
Experience with HLS
  Less code to write and debug
  Fast integration of new features
  Algorithm and architecture exploration possible
  Fast Verification using C++
On-Demand Webinar and White Paper
STMicroelectronics Quickly Brings Automotive Image Signal Processing to Market with High-Level Synthesis
Notes: Why they use HLS
Increase IP value
  Make new features integration more efficient
  Ease the work from C/C++ reference model (algo) to RTL
  Focus on added value = competitive image processing algorithms
Improve Performance Versus mW
  Adapt RTL performance to operating point
  Optimize area for required performance
    JPEG encoder area -13%
    Color filtering algorithm area -31%
    Lens shading correction IP :
      40nm, 1.05V, 375MHz, 32K um2 (22K um2 equivalent 28nm)
      28nm, 0.85V, 400MHz, 12K um2
  Enable very low voltage for power efficiency
Reduce Project Cost
  Accommodate increased complexity of projects
  Reduce initial development time
    3 days to build an optimized dithering IP RTL
  Maximize reuse
  Lower maintenance cost
    1 day to upgrade to an optimized noise reduction algorithm
Experience with HLS
Less code to write = less to debug and maintain
  Ex: jpeg encode, 20k vs 2k lines
  Ex: Renoir (2D rendering), 60k vs 13k lines
1 person can handle a big block
  Ex: bayonet 590kG = 4mm effort
Fast integration of new features
  Ex: HME update to support input down sampling = 3mw
  Ex: Renoir circular buffer = 1mw
Algo and architecture exploration possible
  Ex: Bayonet algo change = 1day
Fast verification using C++
  2000 tests in few minutes (with RTL simulations, ~hours)
  50000 random tests become possible in a working day
  Allows fast iterations when debugging

## Slide 30: Mentor Automotive DRS360 Using Catapult for Both Computer Vision and Neural Networking Acceleration
Sensor Event Detection and Fusion
Semantic Perception
Localization
Situational Awareness
Path Planning
Radar
Lidar
Camera
Sensor
Actuator Control
CatapultC is close to SW development
  It is C++ with more constraints
3x SW engineers on the market than HW engineers
Ramp up is reduced dramatically
Produce deployable PoC in short delays
Optimize for production when final requirements are set
 | Classic Development | With CatapultC
Image Filtering | 2 man/week (expert) | 1 man/week (beginner)
Features Detection | 2 man/week (expert) | 1 man/week (intermediate)
Neural Network (FF) | 2 man/week (expert) | Few hours

## Slide 31: Summary
Next generation AI algorithms are massively complex
Delivering optimized RTL with the best PPA on time is very difficult
  Achieving the most optimal architecture is hard to do in hand-code RTL
  Going from AI development platform to RTL is not well understood
  Verify the RTL is too time consuming
    Billions of computations
    Massively parallel hardware
Catapult and Veloce provide a push-button path from high-level model to rapidly verified RTL