## Slide 1: Efficient use of Virtual Prototypes in HW/SW Development and Verification
Rocco Jonack, MINRES® Technologies GmbH
Eyck Jentzsch, MINRES® Technologies GmbH

## Slide 2: Agenda
Virtual prototype by example
VP use in HW Development
VP use in SW Development

## Slide 3: Virtual prototype by example
Eyck Jentzsch

## Slide 4: Motivation
Usage of VP is beneficial as part of cyber-physical systems (CPS)
CPS– mixture HW, SW running on that HW and the surrounding system consisting of sensors and actors interacting with environment
Useful for automotive, medical, (I)IoT but also others
VPs allow flexible and early prototyping
This tutorial aims to illustrate these statements

## Slide 5: Overview
The Virtual Prototype shown implements a Brushless-DC (BLDC) motor control
As such it contains analog and digital components interacting with each other
There are 2 flavors of the VP:
  a pure digital model solely using SystemC
  a analog/mixed signal (AMS) model using SystemC/AMS

## Slide 6: Structure of the Platform
The model consists of
Motor & load model
ADC, H-Bridge
Microcontroller
  Peripherals
  Interconnect
  RISC-V ISS
system environment/test bench
6
Wrapper
RISC-V ISS
UART
UART
GPIO
PWM
SPI
RAM
PLIC
HiFive1
H-Bridge
ADC

## Slide 7: System components
BLDC Motor model
  Ordinary Differential Equation (ODE) model solved using Runge-Kutta method with fixed step width
H-Bridge
  simplified Switch Model
Analog Digital Converter (ADC)
  8-channel 10bit ADC with SPI Interface
  equivalent to MCP3008
HiFive1 microcontroller platform
system environment/test bench
7
H-Bridge
ADC
HiFive1

## Slide 8: HiFive1 Platform components
Peripherals
  register accurate
  functionality and timing implemented as needed
Interconnect
  loosely-timed router
Wrapper
  SystemC Wrapper containing pure C++ based ISS of RISC-V
8
Wrapper
ISS
UART
UART
GPIO
PWM
SPI
RAM
PLIC
HiFive1

## Slide 9: RISC-V – Some Background
HiFive1 is the first incarnation of the RISC-V Instruction Set Architecture
  developed by SiFive, a company established by the creators of the RISC-V ISA
  implements the RV32 base instruction set (I) together with the M (Integer multiplication) and C (compressed instructions) extensions
  There are ports of the design to Xilinx Artix chips
RISC-V ISA is open source (governed by the RISC-V foundation) and there are plenty of open- and closed-source IPs and tool chains
Further information can be found at https://riscv.org/

## Slide 10: RISC-V – Some Background
There are several ISS available. e.g
  Spike – the reference simulator but too slow for SW development
  QEmu – very fast DBT based ISS but GNU license restrictions limit commercial use
  RV8 – DBT based full-system ISS, difficult to tailor to ISA modifications, limited debugging capabilities

## Slide 11: DBT-RISE based RISC-V ISS
Alternative: DBT-RISE-RISCV
  BSD licensed open-source
  fast ISS (suitable for SW development)
  easy to extend and tailor to ISA combinations and extensions
  easy to integrate into SystemC simulations
builds on DBT-RISE, an infrastructure and library for rapid implementation of DBT based instruction set simulators

## Slide 12: DBT-RISE-RISCV ISS
‘full-system’ simulator based on DBT-RISE
uses dynamic binary translation to achieve high simulation speed
instruction accurate with cycle estimation
SystemC Wrapper
RV32
IMAC
VM
RV32
IMAC
VM
ADAPTER
GDB ADAPTER
SERVER
ARCH
generated out of a DSL describing the machine instructions
  fast turn-around times when changing/extending the ISA
  well suited for HW/SW co-design & exploration

## Slide 13: DBT-RISE based Implementation Flow
UART
VM
ADAPTER
GDB Adapter
SERVER
ARCH
UART
GPIO
SPI
PWM
RAM
system environment/test bench
PLIC
HiFive1
Target specific C++
RV32IMAC: ~ 1.5k LOC
Generated C++ RV32IMAC: ~ 6k LOC
Core Specification
SystemC Platform Model
DBT-RISE ISS
DBT-RISE
~ 5k LOC
Core DSL
RISC-V: ~ 500 LOC
Platform Spec.

## Slide 14: Implementation details
SystemC Configuration and Control Interface used to configure the entire design
Transaction tracing using SystemC Verification Library (SCV)
Modeling blocks taken from SystemC Components library (SCC) available at https://git.minres.com/SystemC/SystemC-Components
Register implementation generated from SystemRDL description
Source available at https://git.minres.com/DVCon2018

## Slide 15: Demo

## Slide 16: VP use in Hardware development
Rocco Jonack

## Slide 17: Motivation
VP model usage for hardware design
  Software driven testing
  Augmentation of HW tests with realistic stimulus
  Bridging gaps in model availability
Different abstraction level imply different requirements
  Mixing abstraction levels is powerful
  Planning of reasonable use models is required

## Slide 18: Modeling abstractions
Behavioral/untimed
  Used for algorithm modeling
Functional/loosely timed (LT)
  Used for SW interaction, also called programmers view (PV)
  virtual prototyping (VP)
Cycle-accurate/approximately timed (AT)
  Used for architectural modeling, also called architecture view (AV)
Register-transfer-level
  Link into verification domain
Notes: Eyck

## Slide 19: Functional/loosely timed (LT)
The loosely timed model is a structural and behavioral refinement of the functional model.
Mapping of functional blocks to HW and SW components and communication interfaces in-between based on a chosen architecture
Subsystems can execute ‘ahead-of-time’
CPU
ACCEL
OS+SW
MEM
I/O

## Slide 20: Cycle-accurate/approximately timed (AT)
Approximated timing on bus communication and on hardware resource access
  Interface communication time
  Average processing time in hardware IP
Transactions are broken down into a number of phases corresponding much more closely to the phasing of particular hardware protocols
CPU
ACCEL
OS+SW
MEM
I/O

## Slide 21: Pin accurate models - RTL
Pin accurate in SystemC
  Adapter between transactions and pin level
  RTL simulators support pin level interfaces for standard types
  Requires typically usage of simulator provided library versions and compilers
Verification effort
  RTL models are typically more detailed and require more attention to details
Bridging multiple abstractions levels introduces need for interpretation
CPU
ACCEL
OS+SW
MEM
I/O

## Slide 22: Integration environments for testing
Standalone testing environments
  Easier analysis and debugging
    Lighter/faster environments
Reuse of common transactors
  Using common components like TLM2 BFMs and memories
    Productivity libraries
Links to tools and open source projects
  C based environment allows easy integration
DUT RTL
DUT AT
TB
TB
Notes: Verification View model VV : embeds a complete RTL description of ICN that is wrapped in order to provide the same TLM2.0 compliant interface as other models
Cycle and bit-accurate, including service network functionality

## Slide 23: RTL components integrated into example system I
Replacing some components with RTL through TLM2pin adapters
  Mix allows stepwise refinement of prototype
system environment/test bench
23
Wrapper
RISC-V ISS
UART
UART
GPIO
PWM
SPI
RAM
PLIC
HiFive1
H-Bridge
ADC
Notes: Verification View model VV : embeds a complete RTL description of ICN that is wrapped in order to provide the same TLM2.0 compliant interface as other models
Cycle and bit-accurate, including service network functionality

## Slide 24: RTL components integrated into example system II
Replacing some components with RTL through TLM2pin adapters
  Mix allows stepwise refinement of prototype
system environment/test bench
24
Wrapper
RISC-V ISS
UART
UART
GPIO
PWM
SPI
RAM
PLIC
HiFive1
H-Bridge
ADC
Notes: Verification View model VV : embeds a complete RTL description of ICN that is wrapped in order to provide the same TLM2.0 compliant interface as other models
Cycle and bit-accurate, including service network functionality

## Slide 25: Demo

## Slide 26: Recommendations
Use common interfaces for bridging between abstraction levels
  Preferably well known and standardized interface like AMBA, OCP
Use libraries of common components
  Productivity libraries decrease turnaround time
  Tools often contain useful components but also imply specific infrastructure
Planning and testing of components
  Functionality requirements
  Speed requirements
  Debugging and analysis
Dynamic switching between abstraction levels is very powerful
Notes: Eyck

## Slide 27: Architectural exploration & performance analysis
Mapping of a behavioral model to one or more points in the architectural space consisting of different HW implementations
Evaluation based on performance characteristics for different system architectures, such as a HW/SW split, communication system, or system components
Typical use case for platform authors
Important properties: accuracy wrt. to performance metrics i.e. timing, latency, throughput, power
CPU
ACCEL
(F1)
OS+SW
(IF, F2)
MEM
I/O

## Slide 28: Tool Flow
Exploration
use case performance
Synthesis
P&R
Timing
traffic scenario
Floorplan Estimation
routing
congestion
Structure
RTL, SystemC
IP-XACT
scripts / constraints
Specification
sockets
domains
memory map
Architecture
switch topology, QoS
buffers, serialization,
pipe stages
floorplan
outline
Verification
testbench
tests
area estimate

## Slide 29: AT Simulation
NoC Model
Traffic
Scenario

## Slide 30: RTL Simulation
RTL
Traffic
Scenario
Running RTL model provides full signal access
Reuse of traffic scenarios

## Slide 31: Recommendations
(re-)using a VP for different purposes needs careful planning
critical components need to provide the important information and accuracy
component in different representations need to be compatible wrt. to communication, build settings etc.

## Slide 32: VP use in Software development
Eyck Jentzsch

## Slide 33: Test-Lab vs. VP
Notes: Eyck

## Slide 34: Test-Lab vs. VP
A classical Test-Lab uses Hardware-in-the-loop (HiL)
  HiL requires expensive Test-Equipment and space
  Bring-up of the lab setup is usually time consuming
Virtual Prototype is a simulation providing FW a runtime environment
  Test-Suites don’t need much space, just a work station or compute server
  Test-Suites can be scaled easily by adding compute power
  Simulations are reproducible
  internal states can easily be traced
  Environment can be stressed easily
  Simulation can be executed virtually “anywhere”
Notes: Eyck

## Slide 35: Anatomy of a VP Test Suite
Hardware (VP)
Firmware
Environment
(VP test bench)
Test Case
Tool-Chain
(i.e. Docker,
LXC, LXD)
Test Suite
Notes: Eyck

## Slide 36: Anatomy of a VP Test Suite
A Test-Suite works as follows:
  Fetch the source code repositories
  Start Container containing stable and host-independent tool-chain
  Build Firmware
  Build VP
  Build Environment/test-bench
  Run the test case(s)
  Evaluate test case execution and collect results
Source: https://stefanprodan.com/2016/continuous-integration-with-jenkins-and-disposable-containers/
Notes: Eyck

## Slide 37: Integration-Aspects
Tool-Chain (i.e. Third-Party libs, Compiler version) can be switched back and forth (i.e. by using different container images)
Run different FW-Versions on same HW (VP)
Run same FW-Version on different HW (VPs)
Failing tests are always reproducible and (i.e. in a Debug-Session on developers computer)
Internal states can be traced (VCD, Trace- and Log-Files)
Notes: Eyck

## Slide 38: Short Demo

## Slide 39: Stressing the Environment
The VP-Environment is a just a model as well
A virtual environment can stress your system beyond reality
Loads can be applied arbitrarily
Stress the environment (VP-)Model to push FW into corner cases
Whenever a random scenario causes a failure, the scenario can be reproduced
Notes: Eyck

## Slide 40: Code-Coverage
An embedded system doesn’t give users much insight into the system (e.g. CPU states, program counters)
therefore coverage collection is difficult
VP-Simulations support Code- and (in some cases) Branch-Coverage collection
Contributors (Test-Cases) to overall Code-Coverage can be identified to streamline testing
Notes: Eyck

## Slide 41: Continuous Integration
A VP-Test-Suite can easily be combined with Git/Gerrit
  Run selected VP-Tests upon every FW-Code-Commit e.g. highest contributors to code coverage
  Run full VP-Test-Suite over night
  Generate FW-Releases e.g. ‘nightlies’
Ensures to have stable working mainline
Combined with a FW test plan it allows to monitor implementation progress
Notes: Eyck

## Slide 42: Benefits of using VP based SW development
Each SW change is tested before propagating to the main line of development
Allows close monitoring of the eSW development progress
effort of VP development pays off esp. when consistently used in SW development even after the availability of the HW
Maximum benefits in situations where one software system addresses multiple hardware variants in different system contexts

## Slide 43: Questions