## Slide 1: Multi-Variant Coverage: Effective Planning and Modelling
Vikas Sharma – Mentor, A Siemens Business
Manoj Manu – Mentor, A Siemens Business

## Slide 2: Agenda
Introduction
Motivation
Application
Challenges
Recommendation
Planning
Implementation
Maintenance
Summary

## Slide 3: Introduction
Traditional Coverage Driven Verification (CDV)
  Involves verification planning and management
Coverage Analysis
Done or Revisit
Test Vectors
Stimulus
Modify Stimulus
Modify Coverage Collector
Merged Coverage Database
Read Functional Specification
Build Verification Plan
XML/XLS
Coverage Collector
Signoff
Maintenance or Next ?
Planning & Implementation

## Slide 4: Motivation
Simple Coverage Model
  Tightly coupled with verification Intents
  Rewrite happens when intent changes
Read Functional Specification
Build Verification Plan
XML/XLS
Coverage Collector
Planning & Implementation
What happens when intended approach changes from compliance to exhaustive ?
What happen when intended IP-version changes from version-1 to version-2 ?
What happens when intended hierarchical context changes from block to SoC ?

## Slide 5: Application
Where DUT has multiple different verification goals targeting different verification intents
The verification goals and intents may change due to variation in
  Exhaustiveness of the verification ( conformance, exhaustive, and application )
  Design specification version ( PHY-v1, PHY-v2, STACK-v1, and STACK-v2 )
  Application specific features ( configuration read write, data streaming, DDR mode )
  Hierarchical instantiation context ( block-level and SoC-level )
MIPI ecosystem of camera, display and PHY’s
Memory and Flash models with multiple vendors and part numbers

## Slide 6: Challenges
To configure desired intents seamlessly
To add coverage and intents for new versions
  Introduction of completely new functionality (Additional application layers)
  To accommodate unforeseeable future extensions (Additional traffic classes)
To provide coverage support for previous versions as well
Traditional approaches doesn’t help
  Multiple coverage models with one for each intent
  Single coverage model with multiple compiler directives controlling intents
  Verification planning tools with exclude options of undesired intents

## Slide 7: Recommendation (Efficient Model)
Multi-Variant Coverage Model
  Intermediate layers are introduced to process and resolve intents
  Intents may have logical relationships
Read Functional Specification
Build Verification Plan
XML/XLS
Coverage Collector
Intent Resolver
Intent File Configuring Coverage Collector
Planning & Implementation
Multiple Intent files can be maintained for capturing different approaches
Multiple Intent files can be maintained for different IP-versions
Multiple Intent files can be maintained for block-level and SoC-level
Multiple Intent Files
Resolved Intent File

## Slide 8: Planning (Example MIPI)
MIPI ecosystem of camera, display and PHY’s
  Includes a combination of protocols whose dynamics change quickly
  Every layer has different versions allowing mix and match
  Involves multiple coverage variants targeting different verification intents
  Has more combinations of PHYs, protocols and their applications with varying versions
  There can be many more verification intents of interest, depending on requirements

## Slide 9: Planning (Report MIPI)
 | Combo D-PHY | Combo C-PHY | Camera D-PHY | Camera C-PHY | Display D-PHY | Display C-PHY
Possible Intent 1 | Version 1.3 | Version 1.3 | Exhaustive | Exhaustive | Exhaustive | Exhaustive
Possible Intent 2 | Version 2.0 | Version 2.0 | Conformance | Conformance | Conformance | Conformance
Possible Intent 3 | Low Power | Low Power | High Resolutions | High Resolutions | High Resolutions | High Resolutions
Possible Intent 4 | Data Rates | Data Rates | SoC Level | SoC Level | SoC Level | SoC Level

## Slide 10: Planning (Example FLASH)
Memory and Flash models with multiple vendors and part numbers
  Involves multiple vendors and part-numbers
    Common in terms of erase/write/read procedures, data strobe, latency, timing information, refresh techniques, OTP techniques, and status and configuration registers
    Differs in terms of memory density, data width, addressing mechanisms, protection levels, operating speed, I/O type, and applications
  There can be many more verification intents of interest, depending on requirements

## Slide 11: Planning (Report FLASH)
 | Winbond | Micron | Macronix | Cypress
Possible Intent 1 | Part W25Q64FW | Part MT25QU512BB | Part MX66L1G45G | Part S25FL512S
Possible Intent 2 | Part W25Q128FW | Part MT25QU01GBBB | Part MX66L51245G | Part S70FL01GS
Possible Intent 3 | Exhaustive | Exhaustive | Exhaustive | Exhaustive
Possible Intent 4 | Basic Read/Write/Erase | Basic Read/Write/Erase | Basic Read/Write/Erase | Basic Read/Write/Erase
Possible Intent 5 | Single/Dual/Quad/Octal | Single/Dual/Quad/Octal | Single/Dual/Quad/Octal | Single/Dual/Quad/Octal

## Slide 12: Implementation
Specify the intents carefully
  Should be specified at higher abstraction
    <intent-file> contains intent names as string type
    <intent-file> file is parsed with system Verilog or scripting file handling mechanisms whichever fits perfectly
    Parsed intents are saved in associative arrays of string type <bit enable_cp[string]>
  Logical relations and expressions can also be specified by adding multiple intents in <intent-file> as Venn-diagrams
    enable_all_coverage
    disable_ddr_coverage

## Slide 13: Implementation
Analyze and process intents
  A simple <intent-file> contains
    List of intents with simple logical relationship
    List of coverpoint and cross names to be enabled
    List of coverpoint and cross names to be disabled
  A complex <intent-file> contains
    List of intents with complex logical relationship
    List of versions, feature list, and much more which might need processing prior parsing via. System Verilog
  Use scripting languages for processing and converting them to a simple <intent-file>
  configures goals and weights of enabled or disabled coverpoints and crosses using `cvg_options

## Slide 14: Implementation
Link <intent-file> with Verification Planner tools
  All major EDA vendors provides verification planner tools for building test-plans (xml or spreadsheet)
  User can change their verification goals which are not of their interests by passing <intent-file> in exclude options
  Explore user manuals because different tool provides a different way to exclude by section and tag lists
  Final verification test-plan shall consist of only intended coverage and merged to universal coverage database.
IP-level
  Coverage should be captured in one super covergroup
  Covergroup may be controlled via. multiple <intent-file>
  Must have a SoC <intent-file> targeting their SoC verification intentions only
SoC-level
  SoC should set global intent as SoC, and may contain a version number, and list of IP’s to be included or excluded
  When an included IP sees the global intent as SoC, then that IP should parse their corresponding SoC <intent-file>

## Slide 15: Maintenance
Key maintenance aspects
  Maintenance of multi-variant coverage model lies in the ability to configure or change intents quickly and reliably
    User-specified intents can be added very easily by making multiple intent-files, saved for future references
  These arguments can be distinguished from other simulator arguments using the plus (+) character.
    +ENABLE_INTENT_FILENAME=<~path/filename.enable>
    +DISABLE_INTENT_FILENAME=<~path/filename.disable>

## Slide 16: Summary
Discussed how a simple coverage model can become a problem in an environment that involves varying verification intents
Demonstrated how a well-captured verification plan can be converted to a working multi-variant coverage model that targets varying verification intents
Multi-variant coverage models that employ these techniques are much easier to reuse and maintain than their counterparts.

## Slide 17: Questions