## Slide 1: Same bits, different meaning – when direct execution based simulation becomes complicated
Evgeny Yulyugin, Intel Stockholm, Sweden
evgeny.yulyugin@intel.com

## Slide 2: Agenda
How does Wind River Simics* simulate CPUs?
VMP technology for direct execution
VMP problem – same bits, different meanings
Simulation speed
*Other names and brands may be claimed as the property of others.

## Slide 3: Instruction Execution in Wind River Simics*
Simics
HOST
Simics
HOST
Simics
Target
HOST
Interpreter
Just-in-Time (JIT) compiler
VMP
Interpreter
Target
JIT compiler
Target
VMP
SLOW
FASTER
FASTEST
*Other names and brands may be claimed as the property of others.

## Slide 4: Wind River Simics* Fall-back strategy
Simics
HOST
Simics
HOST
Simics
Target
HOST
Interpreter
Just-in-Time (JIT) compiler
VMP
Interpreter
Target
JIT compiler
Target
VMP
SLOW
FASTER
FASTEST
Fall back
Fall back
*Other names and brands may be claimed as the property of others.

## Slide 5: VMP technology overview
VMP means VMP
Allows to execute blocks of target code directly on the host
Based on Intel® Virtualization Technology for Intel® 64 and IA-32 architectures
Uses a kernel driver called VMXMON
VMXMON manages hardware resources

## Slide 6: Trap-and-emulate approach
VT-x Guest
VMXMON
Monitor helper
CPU model
Host OS
Wind River Simics*
Hardware
*Other names and brands may be claimed as the property of others.
VT-x = Intel® Virtualization Technology for Intel® 64 and IA-32 architectures

## Slide 7: VT-x Guest
Most of Intel® 64 and IA-32 feature set is available with VMP
  Other fall back to JIT
exits to VMXMON for:
  Not available instructions
  Instructions that must be emulated
  Faults and exceptions (guest)
  Input/Output operations
  External (host) interrupts
  ...
VT-x = Intel® Virtualization Technology for Intel® 64 and IA-32 architectures

## Slide 8: Virtualization assumptions
Instruction classification in Intel® Virtualization Technology:
  Innocuous – can run directly in hardware
  Virtualization sensitive – require simulation

## Slide 9: Virtualization assumptions
Instruction classification in Intel® Virtualization Technology:
  Innocuous – can run directly in hardware
  Virtualization sensitive – require simulation
Regular hypervisor – current guest on current hardware
  All sensitive instruction encodings must be intercepted
Wind River Simics* – future guest on current hardware
  All sensitive, modified and new instruction encodings must be intercepted
*Other names and brands may be claimed as the property of others.

## Slide 10: Vmp problem
Same bits, different meaning

## Slide 11: Intel® 64 and IA-32 instruction format
Intel® 64 and IA-32 Architectures Software Developer’s Manual:

## Slide 12: VMP problem – same bits, different meaning
3rd generation Intel® Core™ i7 (formerly Ivy Bridge) processors or older:
0f
bd
/r
= BSR
f3
0f
bd
/r
= BSR

## Slide 13: VMP problem – same bits, different meaning
3rd generation Intel® Core™ i7 (formerly Ivy Bridge) processors or older:
4th generation Intel Core i7 (formerly Haswell) processors or newer:
0f
bd
/r
= BSR
f3
0f
bd
/r
= BSR
0f
bd
/r
= BSR
f3
0f
bd
/r
= LZCNT

## Slide 14: Test case
Run CPUID (CPU identification) instruction
Check for LZCNT support
Run
Check output register
f3
0f
bd
/r

## Slide 15: Test case
Run CPUID (CPU identification) instruction
Check for LZCNT support
Run
Check output register
Possible results:
f3
0f
bd
/r
 | Old guest | New guest
Old host | OK | Fail
New host | Fail | OK

## Slide 16: Solution
Guest memory:
  Organized in blocks – pages (usually 4k)
  Each page has RWX access right flags

## Slide 17: Solution
Guest memory:
  Organized in blocks – pages (usually 4k)
  Each page has RWX access right flags
Solution:
  Do not allow VMP execution from pages with dangerous instructions
  All other pages can run with VMP

## Slide 18: How to find if a page has a dangerous instruction?
Decode?
  Slow
  Need to known all entry points

## Slide 19: How to find if a page has a dangerous instruction?
Decode?
  Slow
  Need to known all entry points
Pattern matching
  A page with byte sequence is potentially dangerous
  False negatives
f3
0f
bd

## Slide 20: How to find if a page has a dangerous instruction?
Decode?
  Slow
  Need to known all entry points
Pattern matching
  A page with byte sequence is potentially dangerous
  False negatives
  Solution
f3
0f
bd

## Slide 21: Page scanning
Code page classification:
Safe – no dangerous instructions
Unsafe – possibly a dangerous instruction

## Slide 22: Page scanning
Code page classification:
Safe – no dangerous instructions
Unsafe – possibly a dangerous instruction

## Slide 23: Page scanning
Code page classification:
Safe – no dangerous instructions
Unsafe – possibly a dangerous instruction
Safe page
Safe page
Unsafe page
Safe page
Not yet scanned
Address space
f3
0f
bd

## Slide 24: Simulation speed (lower is better)
*Other names and brands may be claimed as the property of others.

## Slide 25: What do we scan for?
By default:
  LZCNT
  TZCNT
Optionally (for performance reasons):
  XSAVE instruction family

## Slide 26: XSAVE state management instructions
Save to/restore from memory processor state components
A state component usually corresponds to an instruction set
XSAVE in VMP is not allowed if guest has state unsupported by host
VMP can intercept XSAVE by disabling it
This will also disable all XSAVE-enabled instructions:
  Intel® Advanced Vector Extensions (Intel® AVX)
  Intel® Advanced Vector Extensions 2 (Intel® AVX2)
  Intel® Advanced Vector Extensions 512 (Intel® AVX-512)
  Intel® Memory Protection Extensions (Intel® MPX)

## Slide 27: Solution for XSAVE problem
Solution:
  Do not allow VMP execution of pages with XSAVE instructions
  All other pages can run with VMP
Safe page
Safe page
Unsafe page
Safe page
Not yet scanned
AVX
AVX
AVX
XSAVE
Address space
AVX = Intel® Advanced Vector Extensions

## Slide 28: XSAVE scanning speedup (higher is better)
Target HW and OS support AVX-512
Host missing AVX-512
Workloads use AVX and AVX2
VMP alternatives:
Disable XSAVE and AVX
Scan for XSAVE and run AVX directly
AVX = Intel® Advanced Vector Extensions
AVX 2= Intel® Advanced Vector Extensions 2
AVX -512= Intel® Advanced Vector Extensions 512
Slowdown because of excluded pages

## Slide 29: Conclusions
Existing direct execution can’t be trusted to simulate future HW
  Alternative is to use JIT and interpreter
Combination of direct execution and described SW technique is required to achieve fast and correct simulation
Adapted VMP roughly 3 times faster than JIT
Adapted VMP compared to original (but unsafe) VMP
  18% slower for OS boot workloads
  27% faster for SPEC CPU2006 benchmarks

## Slide 30: Questions

## Slide 31: Legal Disclaimers
Intel technologies’ features and benefits depend on system configuration and may require enabled hardware, software or service activation. Learn more at intel.com, or from the OEM or retailer.
No computer system can be absolutely secure.
Tests document performance of components on a particular test, in specific systems. Differences in hardware, software, or configuration will affect actual performance. Consult other sources of information to evaluate performance as you consider your purchase. For more complete http://www.intel.com/performance.
Intel, the Intel logo, Xeon, Xeon Phi, Atom, Quark, Core, Pentium, 3D Xpoint, Optane are trademarks of Intel Corporation in the U.S. and/or other countries.
*Other names and brands may be claimed as the property of others.
© 2018 Intel Corporation