## Slide 1: MicroTESK: Architecture Validation Suite Generator for Microprocessors
Mikhail Chupilko, Alexander Kamkin, Alexander Protsenko, Sergey Smolov, and Andrei Tatarnikov
RAS
ISP
Ivannikov Institute for System Programming
Russian Academy of Sciences

## Slide 2: Architecture-Level Validation
Microprocessor implements all instructions of the architecture
Each instruction is implemented correctly
  Single instruction executed in isolation works correctly
  Multiple instructions executed in parallel do not affect each other
    Hazards, memory, exceptions, interrupts, mispredicts, etc.
Microprocessor Design
Architecture (ISA)
conforms (implements correctly)

## Slide 3: Test Program-Based Validation
?
Model or prototype
(HDL, FPGA)
lui a0, 0xdead
ori a0, a0, 0x0
lui a1, 0xbeef
ori a1, a1, 0xf
add t0, a0, a1
sub t1, a0, t1
add t0, t0, t1
Test programs
(ASM)
Reference simulator (C/C++)
Execution traces
(Tarmac)
0x2000: lui ...
0x2004: ori ...
0x2008: lui ...
0x200c: ori ...
0x2010: add ...
0x2014: sub ...
0x2018: add ...
Trace comparator (Python, Ruby)
0x2000: lui ...
0x2004: ori ...
0x2008: lui ...
0x200c: ori ...
0x2010: add ...
0x2014: sub ...
0x2018: bug ...
Test program generator

## Slide 4: Test Program Generator Development
LABEL_4:
lw $2,8($fp)
lw $3,28($fp)
sltu $2,$2,$3
bne $2,$0,$L5
nop
lw $2,12($fp)
addiu $2,$2,1
sw $2,12($fp)
LABEL_2:
lw $3,12($fp)
lw $2,28($fp)
addiu $2,$2,-1
sltu $2,$3,$2
bne $2,$0,$L3
nop
move $sp,$fp
lw $fp,16($sp)
addiu $sp,$sp,24
j $31
nop
LABEL_8:
lw $2,12($fp)
sll $2,$2,3
move $3,$2
lw $2,24($fp)
addu $2,$3,$2
ldc1 $f0,0($2)
sdc1 $f0,0($fp)
lw $2,12($fp)
sll $2,$2,3
move $3,$2
lw $2,24($fp)
addu $4,$3,$2
lw $2,8($fp)
sll $2,$2,3
move $3,$2
lw $2,24($fp)
addu $2,$3,$2
ldc1 $f0,0($2)
sdc1 $f0,0($4)
lw $2,8($fp)
sll $2,$2,3
move $3,$2
lw $2,24($fp)
addu $2,$3,$2
ldc1 $f0,0($fp)
sdc1 $f0,0($2)
LABEL_6:
lw $2,8($fp)
addiu $2,$2,1
sw $2,8($fp)
TEST_PROGRAM:
addiu $sp,$sp,-24
sw $fp,16($sp)
move $fp,$sp
sw $4,24($fp)
sw $5,28($fp)
sw $0,12($fp)
j LABEL_2
nop
LABEL_3:
lw $2,12($fp)
addiu $2,$2, 1
sw $2,8($fp)
j LABEL_4
nop
LABEL_5:
lw $2,12($fp)
sll $2,$2,3
move $3,$2
lw $2,24($fp)
addu $2,$3,$2
ldc1 $f2,0($2)
lw $2,8($fp)
sll $2,$2,3
move $3,$2
lw $2,24($fp)
addu $2,$3,$2
ldc1 $f0,0($2)
c.lt.d $f0,$f2
nop
bc1t LABEL_8
nop
j LABEL_6
nop
?
Instruction set manual
Generation parameters
Instruction sequences
Constraints on data (situations)
Probability distributions (biases)
etc.
Test program generator

## Slide 5: Test Program Generator Requirements
There must not be
  precondition violations: UNPREDICTABLE
  accesses to uninitialized data
  test program infinite looping
There must be possibilities
  to create interesting situations: corner cases
  to generate and embed self checks

## Slide 6: MicroTESK Tool Concepts
MicroTESK-based test generator
Specifications
Translator
Test templates
lui a0, 0xdead
ori a0, a0, 0x0
lui a1, 0xbeef
ori a1, a1, 0xf
add t0, a0, a1
sub t1, a0, t1
add t0, t0, t1
Test programs
Architecture model
Generation core
Generation parameters
Instruction sequences
Constraints on data
Probability distributions

## Slide 7: ISA Specification in nML
type DWORD = card(64)
reg GPR [32, DWORD]
op ADD(rd: R, rs: R, rt: R)
image = format("0000%5s%5s%5s0000100000", rs.image, rt.image, rd.image)
syntax = format("add %s, %s, %s", rd.syntax, rs.syntax, rt.syntax)
action = {
if (NotWordValue(rs) || NotWordValue(rt)) then
unpredicted;
endif;
temp = rs<31>::rs<31..0> + rs<31>::rt<31..0>;
if (temp<32> != temp<31>) then
exception("IntegerOverflow");
else
rd = sign_extend(DWORD, temp<31..0>);
endif;
}
Specification
mode R (i: card(5)) = GPR[i]
syntax = format("r%d", i)
image = format("%5s", i)
action = {
...
}
Registers
Instructions
Addressing modes

## Slide 8: MMU Specification in mmuSL
segment USEG (va: VA) = (pa: PA)
range = (0x0000000000000000, 0x000000007FFFffff)
read = {
if DTLB(va).hit then
tlbEntry = DTLB(va);
elif JTLB(va).hit then
tlbEntry = JTLB(va);
else
exception("TLBMiss");
endif;
...
if v == 1 then
pa.value = pfn<23..0>::va.value<11..0>;
pa.cca = c;
else
exception("TLBInvalid");
endif;
DTLB(va) = tlbEntry;
}
register buffer JTLB (va: VA)
ways = 64
sets = 1
entry = (
R:2, VPN2:27, ASID:8,
PFN0:24, C0:3, D0:1, V0:1, G0:1,
PFN1:24, C1:3, D1:1, V1:1, G1:1
)
index = 0
match = VPN2<26..0> == va.value<39..13>
policy = NONE
address VA (
value : 64
)
address PA(
value : 36
cca : 3
)
Buffers
Addresses
Segments

## Slide 9: Test Templates in Ruby / Python
class MyTemplate < Template
def initialize ... end
def pre ... end
def post ... end
def run
block(:combinator => 'product') {
iterate {
add t0, t1, t2
do situation('Normal') end
add t0, t1, t2
do situation('IntegerOverflow') end
}
iterate {
sub t3, t4, t5
do situation('Normal') end
sub t3, t4, t5
do situation('IntegerOverflow') end
}
}.run
end
end
lui r9, 0x858d
ori r9, r9, 0xc02e
lui r10, 0x58d2
ori r10, r10, 0x7219
lui r12, 0x898a
ori r12, r12, 0x49b7
lui r13, 0x0f31
ori r13, r13, 0xc65a
add r8, r9, r10
sub r11, r12, r13
Prologue / epilogue
Assembly
Special features
Initialization code
Test action
test cases

## Slide 10: Register / Memory Preparators
preparator(:target => 'R', :mask => "0000000000000000") {
or target, zero, zero
}
...
preparator(:target => 'R', :mask => "'b11111111...11111111_1xxxxxxx...xxxxxxxx") {
lui target, value(16, 31)
ori target, target, value(0, 15)
}
...
preparator(:target => 'R', :mask => "XXXXXXXXXXXXXXXX") {
ori target, zero, value(48, 63)
dsll target, target, 16
ori target, target, value(32, 47)
dsll target, target, 16
ori target, target, value(16, 31)
dsll target, target, 16
ori target, target, value(0, 15)
}
lui r9, 0x858d
ori r9, r9, 0xc02e
...
Initialization code
b11111111...11111111_10000101...00101110
(signed 0x858dc02e)
Value-to-mask matching

## Slide 11: Test Generation Techniques
Test data (operand values) generation
  Random generation (range, dist, …)
  Constraint solving (for example, IntegerOverflow)
    SMT-LIB based integration with SMT-solvers (Z3, CVC4, etc.)
Test sequences (instruction streams) generation
  Combinatorial generation (combinator, compositor, ...)
  Subsystem-specific processing (branch, memory, ...)

## Slide 12: Architecture Validation Suite Generation
MicroTESK-based test generator
Specifications
Translator
Test templates
lui a0, 0xdead
ori a0, a0, 0x0
lui a1, 0xbeef
ori a1, a1, 0xf
add t0, a0, a1
sub t1, a0, t1
add t0, t0, t1
Test programs
Architecture model
Generation core
Generation parameters
Instruction sequences
Constraints on data
Probability distributions

## Slide 13: Architecture Validation Suite Generation
MicroTESK-based test generator
Specifications
Translator
Test templates
lui a0, 0xdead
ori a0, a0, 0x0
lui a1, 0xbeef
ori a1, a1, 0xf
add t0, a0, a1
sub t1, a0, t1
add t0, t0, t1
Test programs
Architecture model
Generation core
Autogen
Generation parameters
Instruction sequences
Constraints on data
Probability distributions

## Slide 14: Architecture Validation Test Types
Tests for single instructions
  Boundary values (like RISC-V TVM)
  Specification paths (including MMU)
Tests for multiple instructions
  Short sequences of instructions (like RISC-V Torture)
    Situations (specification paths)
    Dependencies (registers, addresses, etc.)
Tests for multiple types of instructions
  Combination of different test engines (e.g., branches and loads/stores)

## Slide 15: Supported Architectures
Architecture | Project type | Openness | Revision
ARMv8 | Industrial | Closed | AArch64 v8.2
MIPS64 | Industrial | Open | Revision 5
PowerPC | Research | Closed | e500mc
RISC-V | Research | Open | Version 2.2
x86 | Demo | Open | x86-16

## Slide 16: Specification Development Efforts
Architecture | # instructions | # lines of code | Effort
ARMv8 | 1 015 | 18 200 | 30 man-months
MIPS64 | 235 | 4 000 | 4
PowerPC | 122 | 2 800 | 3
RISC-V | 201 | 2200 | 1.5 (w/o MMU)
x86 | 58 | 2 600 | 2.5

## Slide 17: MicroTESK Development Directions
Online test program generation (FPGA, IC)
Architecture-level test coverage estimation
Instruction set simulator generation (QEMU, custom)
Retargetable compilation automation (LLVM, GCC)
Binary code static analysis and deductive verification (SMTLIB, Why3)

## Slide 18
http://www.microtesk.org
microtesk-support@ispras.ru

## Slide 19: Thank you! Questions?