## Slide 1: Advanced Techniques to Accomplish Power Aware CDC Verification
Rohit K Sinha, Intel Corporation
Ashish Hari, Mentor - A Siemens Business
Sulabh Kumar Khare, Mentor - A Siemens Business

## Slide 2: Introduction
Power Management is Critical Today
Driving for finer process technology
  Smaller, lighter products
  Longer battery life
  More functionality
Dynamic power
  Signal switching consumes energy
  Was the major contributor to power consumption
Static power
  Static leakage can consume 50% of power!
  Now the major concern for power optimization

## Slide 3: SOC Power Management Techniques
Leakage Power Reduction is Key in Low-Power Design
Chief Aspects of Power Management
  Power Shut-off
  Isolation
  Retention
  Corruption
  Multiple Voltages  Level shifters
UPF (Unified Power Format)
  Define Power Management independent of design

## Slide 4: CDC verification in presence of UPF
In absence of UPF during CDC analysis, Power control logic is unconnected in RTL
CDC analysis on RTL will not verify power control logic
In presence of UPF with CDC analysis has additional artifacts
  UPF specifies power domain, isolation strategy, retention etc.
Addition of UPF introduces new CDC paths, or break existing CDC synchronizers
  Data loss or data corruption.
  Intermittent CDC errors

## Slide 5: Power Aware CDC verification challenges (Clock, Resets)
Introduction of isolation logic can impact clock and reset paths
Clock and reset paths may become prone to glitches due to the presence of combinational logic
Glitch prone combinational logic on clock path

## Slide 6: Power Aware CDC verification challenges (Isolation)
Introduction of isolation logic can create new CDC paths if the isolation enable signal is driven by an asynchronous clock domain
Isolation logic on a synchronized CDC path can result in combinational logic in the data path that should be guarded against glitches
Broken CDC synchronizer
(Presence of combo logic)
New CDC Path

## Slide 7: Power Aware CDC verification challenges (Retention)
Retention Save & Restore logic can have asynchronous signals driving save and restore, leading to additional CDC paths.
Additional CDC paths created due to retention restore signal

## Slide 8: Case Study
Power Aware CDC analysis flow was tried on a real SoC which contained multiple blocks
3-step hierarchical methodology was followed :

## Slide 9: Case 1: Broken clock path due to isolation control signal

## Slide 10: Case 2: New CDC crossing created due to isolation control signal

## Slide 11: Case 3: Two-DFF CDC synchronizer broken due to additional combinational logic in the TX-RX path

## Slide 12: Power Aware CDC Results
Design | Power Domains | Isolation Cells | Retention registers | Clock Broken | New CDC paths (isolation) | New CDC paths (retention) | Broken CDC synchronizers (combo logic)
subsystem 1 | 3 | 329 | 0 | 25 | 1248 | 0 | 13
subsystem 2 | 15 | 131 | 96 | 8 | 1236 | 1536 | 1

## Slide 13: Conclusions
Low Power issues are missed by traditional CDC methods
Low Power design introduces
  New asynchronous clock domains
  New CDC & VDC paths
Use Power Aware CDC solution to
  Improve low power design reliability
  Avoid low power CDC failures in silicon

## Slide 14: Questions ?