## Slide 1: Intelligent Virtual Platforms
Ola Dahl, Mikael Eriksson, Udayan Prabir Sinha, Daniel Haverås

## Slide 2: Contents
Introduction
Application
Implementation
Results
Conclusions

## Slide 3: Introduction
Uninitialized memory in target code
For host applications, we have tools like Valgrind memcheck and different sanitizers (e.g. MemorySanitizer, AddressSanitizer)
We have a virtual platform, simulating ASICs and board components
Can we instrument the virtual platform, by adding Valgrind memcheck (or sanitizer) like functionality?
If yes, then we could detect usage of uninitialized memory (and more, e.g. memory leaks and access violations) in a non-intrusive way

## Slide 4: Introduction
Concurrency problems in target code
For host applications, we have tools like ThreadSanitizer
We have a virtual platform, simulating ASICs and board components
Can we instrument the virtual platform, by adding ThreadSanitizer like functionality?
If yes, then we could detect concurrency problems in a non-intrusive way

## Slide 5: Application
Figure 1 - Ericsson Radio System products.

## Slide 6: Application
Figure 2 - Ericsson DSP architecture (left) and Virtual platform architecture for DSP simulation (right).

## Slide 7: Memory management error detection
Useful ingredients
Execution of target code on a simulated hardware platform – this we have, in our virtual platform
Knowledge of target program source code – target debugger has this knowledge
Knowledge of the operating system – this information is possible to retrieve from the target operating system (run-time and off-line)
Detection, and reporting, of uninitialized memory usage – this we have implemented (using inspiration from Valgrind and MemorySanitizer)

## Slide 8: Concurrency error detection
Useful ingredients 1-3 from previous slide apply, we also need to
Implement detection and reporting mechanisms – this we have done, taking inspiration from ThreadSanitizer (v2)

## Slide 9: Implementation
Memory management error detection
A-bits and V-bits as in Valgrind and MemorySanitizer
Multi-process and Multi-processor
In some areas we have more accurate detection e.g. flag handling and arithmetic operations
Concurrency detection
Extended happens-before algorithm with memory access tracking as in ThreadSanitizer
Detects data races in a shared physical address space

## Slide 10: Results

## Slide 11
Figure 3 - Detection of uninitialized memory, non-accessible memory, and illegal parameters to system calls.

## Slide 12
U32 offset = 0;
do {
U32 block_size = (size > MAX_BLOCK_SIZE) ? MAX_BLOCK_SIZE : size;
EOS_BlockCopy(dst_p + offset, src_p + offset, block_size);
offset += block_size;
} while(offset < data_size);
Report: DSP=0: PID=65535: Detected inaccessibility in background: SM access
@PCE=0x977b @SM=0xf2e7d-0xf2e8f
Reason: SM is accessed at a location where there is neither a global
variable, nor a heap allocation.
We copy too much data

## Slide 13
for (U16 i = 0; i <= ARRAY_SIZE; i++) {
value = array[i];
if (value == requested_value) break;
}
Report: DSP=0: PID=65535: Detected invalidity: Condition (accumulator flags)
@PCE=0x8cde (invalid bits: 0x400)
Reason: An uninitialized value is used to make a decision on which execution
path to take.
Indexing outside of the array

## Slide 14
Accessing shared data without semaphore protection

## Slide 15: Conclusions
Instrumented virtual platform for
  Memory management error detection
    Uninitialized memory, non-accessible memory (e.g. stack and heap handling), uninitialized parameters to system calls
    Developed for production usage
  Concurrency error detection
    Data race detection in a shared physical memory (prototype implementation)
Multi-process and Multi-processor
Re-using many ideas from Valgrind, MemorySanitizer, ThreadSanitizer
Non-intrusive implementation inside a virtual platform (no impact on target application timing, no impact on target memory usage)
Host execution speed impact of 2-4x (memory management error detection – tests on a set of small programs) and 5x (concurrency error detection – initial tests)

## Slide 16: Questions