## Slide 1: Generating Bus Traffic Patterns
Jacob Sander Andersen, CTO, SyoSil ApS, jacob@syosil.com Lars Viklund, Expert Engineer, Axis Communications AB lars.viklund@axis.com Kenneth Branth, Senior Consultant, SyoSil ApS, kenneth@syosil.com

## Slide 2: The Challenge in Short
Verification engineer required to apply a specific traffic pattern on a hardware bus like AMBA AXI
Why?
  Functional requirements (e.g. performance requirements)
  Verification closure (E.g. metrics like structural coverage)

## Slide 3: Motivation
Verification Workshop
Initial scenario…
  Designer:
    Answers questions 
  Verification engineer:
    Ask questions
    Takes notes in informal language
    Does the implementation
2nd try…
  Designer:
    Answers questions 
  Verification engineer:
    Ask questions
    Defines transaction diagram
    Does the implementation

## Slide 4: Core Problem, Consequence & Solution
Communication between designer and verification engineer
  Information loss
  Leading to incorrect implementation
Consequence
  Many iterations
  Loss of productivity (Wasting designer and verification engineers time)
Solution
  Let the designer express the traffic pattern directly and accurately

## Slide 5: Example
Setup
  Hardware with an interface connected to an addressable memory
  Interface capable of doing reads and writes
Two buffers in the memory
  BUF0
  BUF1
Memory Map
BUF0
BUF1

## Slide 6: Example
An example of a specific traffic pattern:
  Producer A: Reads to BUF0.
  Producer B: Writes to BUF0.
  Producer C: Writes BUF1 with a simple synchronization between them to ensure that producer C starts only after producer A has done 4 transactions.
Producer A
Transactions
1
3
2
1
3
1
2
3
4
5
Producer B
Transactions
1
2
3
Producer C
Transactions
1
2
3
4
5
Interface
4
1
2
2
5
3
4
5
Traffic Pattern

## Slide 7: Road to an Abstraction (As always )
An abstraction of the example is needed
Provide designer with ability to express such traffic patterns
Source/Sink model
  Each producer is a source
  Sink is the interface
  The cloud represents
    Synchronization (E.g. between sources)
    Scheduling
Source 0
Source 2
Source 1
Synchronization/ Scheduling/etc.
Sink

## Slide 8: But wait!!!
Is this not just PSS?
Both yes and no..
  Some traffic patterns could be captured by PSS
  This is targeting fine grained control of transactions on a single (or multiple) interfaces
    Very specific scenarios for coverage closure
    Very specific scenarios for performance verification

## Slide 9: Transaction Sequence Model
The transaction sequence model (TSM) refines the source/sink model
Replacing sources with transaction producers (TPs)
  The TPs generate the transactions when requested
Replacing “The cloud” with
  Transaction Sequence graph (TS graph)
    Captures synchronization etc.
    Nodes are of the type transaction sequence elements (TSEs)
  Scheduler(s)
The bus traffic pattern at the sink
  Generate transactions by traversing the TS graph
= State
TSM
TP
TP
TP
TS Graph
TSE
TSE
TSE
Scheduler
Scheduler

## Slide 10: Transaction Sequence Elements (TSE)
The TSE nodes needs to capture the synchronization, scheduling etc.
Node examples
  TST: Request a transaction from a given producer (TP)
  TSS: Sequencing of TSEs
  TSP: Parallelism of TSEs
  TSR: Repetition of TSEs
TSE state example
  Number of started transactions
  Number of ended transactions
TSE function example
  ended(<N>)
  terminated()

## Slide 11: TSE Example: TSR
tsr(tse, N)
  Parameters:
    tse (TSE node) – Node to be evaluated N number of times.
    N (integer) – The number of iterations. 0 indicates infinity.
  Return type: Returns a TSR node.
TSR.termimnated()
TS
TS
TS
Time
0 1
0 0
Producer
<TSR>::=TSR(<TSE>, <N>)
Any other transaction sequence element
Number of repetitions
TSR(TS, 3)

## Slide 12: Implementation: DSL or Not?
One could implement a DSL capturing the TSM
  Scanner and parser needed
Instead
  Specify the abstract syntax tree (AST) directly
  Embedded DSL (eDSL)
  Obvious benefit: no scanner and parser 

## Slide 13: AST/eDSL Example
"""
AST/eDSL Example
"""
tp0 = tp0('tp0', 5)
tp1 = tp1('tp1', 3)
tp2 = tp2('tp2', 5)
sch = scheduler_weight('WEIGHT’, [1, 1, 1]);
tst0 = TST(tp0)
tst1 = TST(tp1)
tst1 = TST(tp2)
tsr0 = TSR(tst0)
tsr1 = TSR(tst1)
tsr2 = TSR(tst2)
tsw = TSW(tp0.ended() == 4)
tss = TSS([tsw, tsr2])
root = TSP(sch, [tsr0, tsr1, tss], tsr0.terminated() && tsr1.terminated() && tss.terminated())
TP definitions
Scheduler definition
Equally weighted
TS graph reference to TPs
Repetition, no need for N as the producers know their limit
Root of the TS graph with termination criteria
Wait for tp0 to have produced 4 transactions

## Slide 14: Implementation
Generator
AST BCL
AST Instance
AST Instance
Synchronization Object
AST BCL
Virtual Sequence
AST Traversing Algorithm
SV, AST instance specific
SV, Reusable
Python, AST instance specific
Python, Reusable

## Slide 15: Traffic Pattern Generation
Create uvm_test which starts the generated virtual sequence
Virtual sequence
  Executes AST traversal algorithm
  Three outcomes:
    WAITING: The AST cannot produce a transaction. Wait until synchronizer okay’s reevaluation
    READY: Can produce the next transaction
    TERMINATED: Done for the day
  When READY then a transaction is provided which can be applied on the bus using the appropriate UVC
The result should be a trace of the requested traffic pattern being applied to the bus

## Slide 16: Conclusions
A portable and executable specification of traffic patterns has been defined
Using an eDSL removes a significant maintenance burden
Using a tree traversal algorithm provides support for multiple target platforms (UVM, SystemC, etc)
Framework can be extended to handle:
  Multiple sinks
  Load balancing on other aspects than number of transactions, e.g. amount of data or any other meta data

## Slide 17: Questions
Finalize slide set with questions slide