## Slide 1: Portable Stimulus Driven SystemVerilog/UVM verification environment for the verification of a high-capacity Ethernet communication endpoint
Andrei Vintila, AMIQ Consulting
Ionut Tolea, AMIQ Consulting

## Slide 2: Introduction
Block
Requirements
Traditional Approach
PSS Approach

## Slide 3: Example System

## Slide 4: Recap of system features
Bidirectional traffic:
  TX
  RX Correct
  RX Corrupted
Control block: Configured/Not configured
  Enables the TX traffic capability of the system
Filtering block: Configured/Not configured
  Enables the system capability of discarding corrupted traffic

## Slide 5: Requirements
Verify all data paths
  Different types of packet characteristics
  Different types of configuration for the blocks
  Different blocks configured / Different interfaces driven
Ensure the re-usability of the TB

## Slide 6: Traditional approach
Re-use VIPs between TBs
Re-use TBs between projects
Re-use infrastructure from block level TBs
Create individual testcases for each interesting scenario

## Slide 7: Issues
Creating dependencies between TBs
  Different layers of integration
  Missing a good management of what can be re-used
    Compatibility between block level TBs
    Block level specific implementation
A huge number of testcases implemented
  Small deviations in traffic/configuration -> New scenario
  Directed testcases -> Non-reusable logical layer sequences

## Slide 8: Idea behind PSS approach
Break the functionality of the system in modular actions
Offer a software view when simulating RTL
  A system feature translates in multiple software actions
  Each software action has a correspondent in hardware stimuli
  Hardware stimuli take a different form on each layer of integration
The PSS model puts constraints on the implementation quality
  Increase re-usability
  Lower debug time

## Slide 9: PSS as an abstraction layer
Better control for directed scenario definition
Better planning for verification strategy
Ease testcase portability across multiple layers of integrations and platforms

## Slide 10: Guidelines
Encapsulate run-time configuration in actions
SystemVerilog/UVM sequence layering should be used to bridge gaps between transaction level sequences and system level actions
Synchronization and timing should translate into actions on PSS layer and event triggers on SV layer
Coverage and logical constraints -> PSS Layer
Protocol constraints -> SV Layer

## Slide 11: Implementation

## Slide 12: Generated Scenarios 1

## Slide 13: Generated Scenarios 2

## Slide 14: Project Application
Replace directed testcases with PSS based test generation
Ease debug with scenario flow view
A tighter infrastructure for verification which favors re-use

## Slide 15: Conclusions
PSS standard has all the necessary features to accommodate a higher abstraction layer over a SV/UVM environment.
Due to extensive support for PSS tools, this approach bridges the communication gap between verification engineers and system architects
A general recipe can be defined for VE development flow

## Slide 16: Questions