## Slide 1: Qualification of a Verification IP
Francois Cerisier, Adrien Carmagnat, AEDVICES Consulting Alessandro Basili, Gilles Curchod, MELEXIS

## Slide 2: Agenda
Introduction
VIP Qualification
Use Case: the SENT protocol
Considerations on Mutation Testing
Qualification Plan
Qualification Tests
Need for a Qualification UVM Library
Qualification Library Usage
Conclusion

## Slide 3: Introduction: Needs for VIP Qualification
Safety Critical Standards requires that tools are qualified
  DO254, ISO26262: Design tools and verification activities need to be qualified
  Qualification should be done on per-project basis
VIPs are key parts of the overall verification process
  Is it a tool ?
  Is it the part of the verification environment ?
VIPs user experience is not enough to guarantee they are good !
How to ascertain a VIPs is good ?
How to know if VIPs can report protocol violations ?
 Qualification of the VIP

## Slide 4: Use Case: SENT VIP
SENT: Single Edge Nibble Transmission for Automotive Applications
Standard: J2716™ from SAE International
Transmission of pulses over a single line
Encoding made of pulse duration
Frame
  Sync Pulse
  Comm Nibble
  Data Nibbles
  CRC Nibble
  (Pause Nibble)
Source: J2716™ SAE Internaltional

## Slide 5: Use Case Qualification
How good is the VIP ?
How can I trust it ?
Will my VIP trigger assertions on any protocol violation ?
How can I benefit from qualification from other projects reusing the same VIP ?
   Can I qualify the VIP by itself ?

## Slide 6: Limitation of Mutation Testing
Qualification 1st idea:
  Apply mutation testing
Mutation Testing:
  Automatic Test Bench Qualification
  Globally Qualify if a testbench let bug escape
  Testbench
    VIP + Scoreboards + Assertions +Self Checking Tests + …
Problems:
  Traceability
  How to judge the protocol aspects themselves ?
  Are mutations good for VIP qualification ?
DUT
Random Mutation
propagation
activation
VIP
VIP
Scoreboard
Test Bench

## Slide 7: Verification IP features and Qualification Needs
Stimulus Generation:
  Ability to generate the tests
  Qualification: Can be done in the project pass/fail criteria, per result analysis and reports
Functional Coverage:
  Ability to collect protocol information
  Qualification: make sure that monitors collect the right information
Protocol Checkers:
  Ability to assert the protocol is correct
  Qualification: make sure that protocol violations are reported

## Slide 8: Protocol Checker Qualification Plan
Qualification Plan:
  Specification Review vs Assertion Review
  Specification Review:
    Need to interprete specification and find areas that require checkers
    Develop a test plan to highlight that assertions exist on any identified point of the spec
  Assertion Review:
    Cross check with Specification Review the existance of the assertion (need Assertion to Spec traceability)
  Develop tests that show that assertions are working as expected
  Expected Behavior = UVM_ERROR

## Slide 9: Qualification Plan
Section | Title | kind | Covers | Description | Link | Type
1 | Global Verification Plan for SENT VIP | title |  |  |  | 
1.1 | Calibration Pulse | title |  |  |  | 
1.1.1 | Calibration Length | VTC | SAE J2716 - Section 5.2.2 | Note : Since protocols allows a ±20% clock period variation a calibration pulse would be considered as valid if its length is inside [ 45;67] ticks length. Goals: - verify that VIP reports an error when calibration length is outside of valid value Test Scenarios: - For various SENT frames with valid low time with different length for the calibration pulse. - Cover cases with length = 56 - Cover case with length 45, 46, 47, 65, 66, 67 and other value inside [45;67]. Checks: - Check that assertions are not triggered when calibration length is inside [45 ; 67] - Check that assertions are triggered if calibration calibration length is < 45 or > 67 | invalid_calibration_lenght_test_seq valid_calibration_lenght_test_seq frame_cg:calibration_pulse frame_cg:calibration_lenght SENT_ASSERT_SYNC_LOW_MIN_TIME | Test Test CoverPoint CoverPoint Assertion
1.1.2 | Calibration low time | VTC | SAE J2716 - Section 5.2.2 | Goals: - verify that VIP reports an error when the five clock ticks of calibration pulse are not driven low Test Scenarios: - For various SENT frames with different low time for the calibration pulse. - Cover cases with low time = 1, 2 ,3 and 4 - Cover cases with low time = 5, 54, 55 and other arbitrary values. Checks: - Check that assertions are triggered if calibration low time is 1, 2, or 3. - Check that assertions are not triggered if calibration low time is > 4. | invalid_calibration_low_time_test_seq valid_calibration_low_time_test_seq frame_cg:calibration_pulse frame_value_cg:low_tu SENT_ASSERT_SYNC_LOW_MIN_TIME | Test Test CoverPoint CoverPoint Assertion

## Slide 10: Protocol Checkers Tests
Write tests that:
  Show nominal functions are working
  Highlight Error Conditions
Check that VIP can report errors
Leads to errors in the log and in the assertion coverage database
How to sort out expected errors from unwanted errors ?

## Slide 11: SENT Protocol Assertion Qualification Example
Test Plan
  Synchronisation just below the minimum limit  UVM_ERROR
  Synchronisation just above the minimum limit  OK
  Synchronisation just below the maximum limit  OK
  Synchronisation just above the maximum limit  UVM_ERROR
56
±Δ
No Assertion fires
Test PASSED
Assert FAILED
Test PASSED

## Slide 12: UVM Qualification Library Spec
Key Features:
  Specify errors that are expected
  Expected Error Monitoring
  Expected Error Callbacks and hooks
  Nice and understandable Report

## Slide 13: UVM Qualification Library Spec
Allows the specification of the expected errors
  To verify design under error conditions (protocol violations, failsafe mechanisms, alarms, …)
  To qualify assertions that shall trigger errors under error conditions
Expected Error Monitoring
  At least N errors, At most N errors
  Time Window during which the error can occur (start, end, duration, event)
  Deal with uncertain grey zone (transition to recovery where error may occur once more)
  Filter: Per checker instance, per checker ID, per message content

## Slide 14: UVM Qualification Library Spec
Expected Error Callbacks and hooks
  Monitor expected errors, possibility to perform actions on expected errors
  Possibility to downgrade expected errors to warnings or info.
Reports
  Caught expected errors  they are OK
  Caught unexpected errors  Real Error to consider as FAIL
  Unseen expected errors  considered as FAIL.
  Possibility to override UVM reports (remove expected errors from summary).
  Seamless integration into any UVM verification framework

## Slide 15: UVM Qualification Library Behavior
Error Setup
Error detected
Is it expected ?
Expected  OK
Report
FAIL
Is it expected ?
Error detected
Is it expected ?
No  standard UVM behavior
Unexpected  KO
Unexpected  KO
Error detected
Return to valid mode
No  standard UVM behavior
End of Expected Error Time Window Did all expected errors occur ?
# ** Report counts by severity
# UVM_INFO : 2
# UVM_WARNING : 0
# UVM_ERROR : 3
# UVM_FATAL : 0
# FOUND EXPECTED_ERROR: 1
# UNFOUND EXPECTED_ERROR: 1
# UNEXPECTED_ERROR: 2

## Slide 16: UVM Qualification Library Behavior
Error Setup
Error detected
Is it expected ?
Expected -> OK
Report
PASS
Error detected
Is it expected ?
Return to valid mode
End of Expected Error Time Window Did all expected errors occur ?
# ** Report counts by severity
# UVM_INFO : 2
# UVM_WARNING : 0
# UVM_ERROR : 2
# UVM_FATAL : 0
# FOUND EXPECTED_ERROR: 2
# UNFOUND EXPECTED_ERROR: 0
# UNEXPECTED_ERROR: 0
Expected -> OK

## Slide 17: Testbench topology

## Slide 18: Colaboration Diagram
uvm_report_catcher
  Default class for UVM messages
  « catches » all messages
aed_report_catcher
  Singleton
  Inherits from uvm_report_catcher
  Attached to all uvm_report_object
    Via uvm_report_cb (callback)
  Filter out the good and the bad !
uvm_report_cb::add( null, aed_report_catcher::get_instance())
Notes: 1
2 - Here we have set an expetation on an UVM_ERROR with id “SENT_ASSERT_SYNC_LOW_TIME” with an error count of 1 and only 1. If dont get this number of error, we will issue an error to make the test failing
3 - As an error on the synchronization can make the ECU to read wrong nibble values, it could make the CRC_VALUE false so we ignore any error on CRC value
4

## Slide 19: Demoter Setup
// Get a new group of message to catch and demote.
msg_grp1 = aed_report_catcher::type_id::get_report_action_group("Group-1");
Create and get an handle on a group
// Set message ID to catch, its minimum and maximum expected occurrences
msg_grp1.expect_error_by_id(
.name ( "QUALIF_ASSERT_SYNC_LOW_MIN_TIME" ),
.id ( "SENT_ASSERT_SYNC_LOW_MIN_TIME" ),
.min ( 1 ),
.max ( 1 ));
Set an expectation on an UVM_ERROR ID
In build phase :
uvm_report_cb::add( null, aed_report_catcher::get_instance())
In test sequence :
Notes: 1
2 - Here we have set an expetation on an UVM_ERROR with id “SENT_ASSERT_SYNC_LOW_TIME” with an error count of 1 and only 1. If dont get this number of error, we will issue an error to make the test failing
3 - As an error on the synchronization can make the ECU to read wrong nibble values, it could make the CRC_VALUE false so we ignore any error on CRC value
4

## Slide 20: Demoter Setup
// Stop the expected error window, no more error expected
msg_grp1.stop();
Start monitoring
// Start the expected error time window
msg_grp1.start();
// Create the error condition
`uvm_do_on_with(req, sensor_sequencer, { req.invalid_sync_pulse == 1;} );
Generate a transaction with the error condition
Stop monitoring window
// Set message ID to ignore within the same time window
// Same as calling expect_error_by_id with minimum=0 and no maximum.
msg_grp1.ignore_error_by_id(.id ( "SENT_ASSERT_CRC_VALUE" ));
Ignore UVM_ERROR with Id SENT_ASSERT_CRC_VALUE
// Set action to perform on these errors: Demote to Warning.
msg_grp1.demote_error ( UVM_WARNING );
Demote errors caught by this group to UVM_WARNING

## Slide 21: Demoter Report
# ====== AED DEMOTER END OF SIMULATION REPORT =====
#
# UVM_ERROR short_path/aed_report_utils/src/sv/aed_report_catcher.sv (314) @ 78933000: uvm_test_top.sequencer@@sent_invalid_test_seq [MIN COUNT NOT REACHED] Filter : QUALIF_ASSERT_SYNC_LOW_MIN_TIME
#
# Number of caught error is lower than min count :
# Actual count : 0 Min expected count : 1
# _____________________________________________________________
# Catcher Name , Expected , Actual , Status
# QUALIF_ASSERT_SYNC_LOW_MIN_TIME , [ 1: 1 ] , 0 , FAIL
# IGNORE_FILTER_SENT_ASSERT_CRC_VALUE , [ >= 0 ] , 1 , OK
# _____________________________________________________________
#
# report_catcher : Group-1: FAILED ; 0 error while expecting at least 1
#
# =================================================

## Slide 22: Conclusion
VIP needs to be trusted
Needs traceability
Needs catching expected errors
Developped Qualification Library + a proper qualification approach can bring trust in the VIP
More than the library, we need the right approach…

## Slide 23: Questions ?