## Slide 1: Methodology for Automated Validation of Analog Behavioral Models for Mixed-Signal Verification
Nan Ni, Chunya Xu, Sebastian Simon
Infineon Technologies AG

## Slide 2: Agenda
Motivation
Theoretical background
  Real number model
  A-UVM (Analog-UVM)
  Metamodeling framework
Flow implementation
Application
Conclusion

## Slide 3: Agenda
Motivation
Theoretical background
  Real number model
  A-UVM (Analog-UVM)
  Metamodeling framework
Flow implementation
Application
Conclusion

## Slide 4: Motivation
Shorten mixed-signal verification time
Reduce simulation run time
Reduce analog model development time
Reduce model validation time
Automation of model generation and validation
Model at higher level of abstraction
Reduce testbench development time
Use real number model

## Slide 5: Motivation
Idea: Automated generation of real number models and corresponding testbench (TB) for validation
Specification of Analog Module
Real Number Model
Validation Testbench
Run Script
Linear Module:
  Linear filter
  Linear amplifier
Nonlinear Module:
  Comparator
  ADC/DAC
Constrained randomized stimulus
Simulators:
Cadence Incisive
Synopsys VCS
Mentor Graphics Questa

## Slide 6: Motivation
Solutions:
1. Use meta-modeling concept for model and testbench code generation
2a. Use UVM-based testbench for validation
2b. Script to run simulation
Problems:
1. Find an efficient way of generating analog models
2. Lack systematic model validation method

## Slide 7: Agenda
Motivation
Theoretical background
  Real number model
  A-UVM (Analog-UVM)
  Metamodeling framework
Flow implementation
Application
Conclusion

## Slide 8: Real Number Model
Advantages of RNM:
digital solver only
mostly faster than verilog-A, verilog-AMS, SPICE
behavioral model, signal flow

## Slide 9: A-UVM = UVM + analog package
Sequencer
Driver
Monitor
Monitor
Analog Module
Scoreboard
Test
Environment
Agent
Agent
Sequence
Trans:
Name: sine/ramp/Fourier/constant
Freq: 200kHz
Ampl: 5
Dur: 5us
…
Trans:
Name: sine/ramp/Fourier/constant
Freq: ..
Ampl: ..
Dur: ..
Model
Monitor
Agent
trans
trans

## Slide 10: A-UVM
Features of A-UVM:
analog constrained-random stimulus
trigger analog transactions
use metrics to compare transactions
support analog functional coverage

## Slide 11
Metamodeling framework
Infineon’s proprietary Metamodeling framework

## Slide 12: Agenda
Motivation
Theoretical background
  Real number model
  A-UVM (Analog-UVM)
  Metamodeling framework
Flow implementation
Application
Conclusion

## Slide 13: Flow implementation
Specification of Analog Module
Real Number Model
Validation Testbench
Run Script
Template for analog models, TB in SV and run script
Step1: make UML diagram for analog model and TB
Step2: prepare Mako templates
Step3: generate metamodeling structure
Step4: give parameters in GUI
Setp5: generate code

## Slide 14: Flow implementation
Top-level UML diagram of the flow:
analog model
A-UVM TB
Step1: make UML diagram for analog model and TB

## Slide 15
Linear filter
Linear amplifer
Linear Module

## Slide 16
UML Diagram of nonlinear Module
Parameters:
Poles
Zeros
Frequency
name
...

## Slide 17
ADC
DAC
Comparator
Oscillator
...
Conversion function:
ADC:
Nonlinear Module

## Slide 18
UML Diagram of nonlinear Module

## Slide 19
UVM Testbench Generation

## Slide 20
Test case and test environment
Test sequence
Test agent
Test scoreboard
UML Diagram of UVM TB

## Slide 21
Mako Template
if (result > ${scb.tolerance} )
`uvm_info(get_type_name(), $sformatf("pass successfully, comparison result: %f", result), UVM_LOW)
else
`uvm_error(get_type_name(), $sformatf("fail, comparison result: %f", result))
<Int_Class_ID>8</Int_Class_ID>
<Scoreboard type="AnalogScb">
<Int_Class_ID>18</Int_Class_ID>
<tolerance>0.95</tolerance>
<InputAnalogAgentRef>9</InputAnalogAgentRef>
<OutputAnalogAgentRef>10</OutputAnalogAgentRef>
<ComparisonAlgo>EmdAlgo</ComparisonAlgo>
</Scoreboard>
if (result > 0.95 )
`uvm_info(get_type_name(), $sformatf("pass successfully, comparison result: %f", result), UVM_LOW)
else
`uvm_error(get_type_name(), $sformatf("fail, comparison result: %f", result))
Spec.xml
Scoreborad.svh (comparison function)
Step2: prepare Mako templates
Step5: generate code
Step3: generate metamodeling structure
Step4: give parameters in GUI

## Slide 22: Agenda
Motivation
Theoretical background
  Real number model
  A-UVM (Analog-UVM)
  Metamodeling framework
Flow implementation
Application
Conclusion

## Slide 23: Application
Modeling Task
ADC RNM generation
TB generation :
Digital output transaction
Analog input transaction(ramp)
Checking result
Modeling Target (analog module)
Multi-ADC in a radar project
Four 11-bit ADCs
IP separately verified
Analog macro provided

## Slide 24: Application
Error Detected Waveform of MADC
Error Fixed Waveform of MADC

## Slide 25: Application
Time Consumption Comparison
 | RNM MADC | RADAR MADC
Simulation Time | 4.5s | 74.1s
Speed up: ~16 times

## Slide 26: Conclusion
Summary
1. Focus on testbench automation for AMS component validation based on Metagen
2. Analog behavioral model generation
3. Application on a radar chip: correct functionality, receive speed up
Future work
1. Integrate model into top-level simulation
2. MDA approach
3. Real number models should support more industrial practical issues: X value propagation, integration check via assertions

## Slide 27: Questions

## Slide 28: Backup slides

## Slide 29
initial beign
my_sys = new;
cons = my_sys.construct(z_complex_vec,z_real_vec, p_complex_vec, p_real_vec );
end
always @(posedge clk) begin
vin_s = vin;
resp = my_sys.get_response(vin_s, T); //response calculation
vout_s = resp * gain;
end
Linear module realization:

## Slide 30
Zmax = $pow(2, n_bit);
xin_0 = adc0_i_p - adc0_i_p;
Dout_zw_0 = Zmax * (xin_0 + vref)/(vref + vref);
ADC function:

## Slide 31
%if (_Module.get_ConvertionFunctionParameter() != 0 ):
counter = 0;
enable_counter <= 1;
%for index in range(port_size):
<% port = _Module.get_list_DataPortInput()[index] %>\
%if (port.get_is_differential() == True):
xin_${index} = ${port.get_name()}_p - ${port.get_name()}_n;
%elif (port.get_is_differential() == False):
} xin_${index} = ${port.get_name()};
%endif
Dout_zw_${index} = Zmax * (xin_${index}+vref) / (vref+vref);
%endfor
…
// calculation of intermediate variables
xin_0 = adc0_i_p – adc0_n;
Dout_zw_0 = Zmax * (xin_0+ref)/ (vref +vref)
Validation Testbench Generation Flow
Mako template
ADC RNM