## Slide 1: Automated Configuration of Verification Environments using Specman Macros
Milos Mirosavljevic, Veriest Solutions, Belgrade, Serbia, (milosm@veriestS.com)
Ron Sela, Valens Semiconductors, Hod HaSharon, Isreal (ron.sela@valens.com)
Dejan Janjic, Veriest Solutions, Belgrade, Serbia, (dejanj@veriestS.com)
Efrat Shneydor, Cadence Design Systems, Petach Tikva, Isreal (efrat@cadence.com)

## Slide 2: Introduction
Problem: increasing ASIC complexity
More lines of RTL code, more gates and more features
Higher logic complexity and more configurations
Verification point of view: how to plan it and organize it for the highest efficiency?

## Slide 3: HDBaseT® At a Glance
Standard for the transmission of ultra-high-definition video & audio, Ethernet, controls, USB and up to 100W of power over a single, long-distance, cable.
Used in audiovisual, consumer electronics, medical and government applications, as well we automotive.

## Slide 4: HDBaseT® Switch (“T-Switch”)
16 x ports with 16+2Gbps per port
Each port supports HDCP 2.2 and HDCP 1.4

## Slide 5: T-Switch – Verification challenges
Cover all different configuration options
Verification team size and different levels of expertise: need easy to use API which solves all configuration matters under-the-hood and allows straightforward test creation
New engineers assigned to the project should be able to start working right away, without the need for excessive environment introduction
Verification environment structure?

## Slide 6: Typical verification solutions
Implementing new verification methodologies
Using advanced code tecnhiques
Power of reusability

## Slide 7: T-Switch – Verification solution
Specman macros – extending e and adding new constructcs
Main advantage – easy to use syntax for test writers
define as
Macro output is called stream – set of rules used by verification environment
Each stream conveys different protocol
16 ports to be configured
256 possibilities of communication between the ports

## Slide 8: ADD_STREAM macro (1)
action macro used under pre-defined run()
Override necessary old configuration generated automatically, just before the first specman tick (sequences need at least 1 tick to start their body)

## Slide 9: ADD_STREAM macro (2)
Quickly create desired scenarios:
  Inject HDMI data to the switch port 0 and send this data through the HDCP towards port 14 and also send it back from port 0 (multicast)
  Inject data with very low bandwidth to the switch ports 0-7, and send this data towards portd 8-15

## Slide 10: ADD_STREAM macro (3)
Simple usage:

## Slide 11: ADD_STREAM macro (4)
Allows designers to create scenarios without Specman knowledge itself
Macro usage: 15 lines of code in the test
Macro instantiation translates to 180 lines of code under the hood: 12x code reduction
Required and optional arguments
Required: stream type, source, destination, hdcp, packet types
Optional: hdmi command, bist termination, hdcp version

## Slide 12: Example scenario – stress test
Stress test: maximum bandwidth throught the chip
Each port: 16G +2G = 288Gbps
Total of 16 ADD_STREAM macros used

## Slide 13: Specman macros advantages
Easier to read – unlike other languages, macro developer defines syntax for end user
Simplicity of usage: easier than functions when there are so many inputs
Function:
Macro parameters can be lists of unknown length:

## Slide 14: Specman macro limitations
Limitation of 14 input arguments
Team utilized mechanism of optional arguments to increase number of inputs
Improvement by ~70% (14->14+10)
Optional arguments allowed much more versatility in stimuli generation
Macro simplification: optional arguments default values

## Slide 15: Results
Macro allowed accelerated verification – tape out on time
Exhaustive coverage achieved
Full leverage of the team: juniors and seniors, as well as designers
Project life span ~ 2.5 years
14 different verification engineers
7 design engineers who sporadically joined verification
185000 registers in ASIC, 279 tests
Macro used in ~75% of the tests

## Slide 16: Results
Presenter:

## Slide 17: Questions?