## Slide 1: UVM mixed signal extensions Sharing Best Practice and Standardization Ideas
Joen Westendorp, NXP Semiconductors
Sebastian Simon, Infineon Technologies AG
Joachim Geishauser, NXP Semiconductors

## Slide 2: Agenda
Introduction - 5 min
UVM Mixed Signal Verification Experience Sharing sessions:
  UVM-MS mixed signal extensions – 30 min
    Joen Westendorp, NXP Semiconductors
  A-UVM — A Transaction-Oriented UVM-Based Library for Verification of Analog Behavior – 30 min
    Sebastian Simon, Infineon Technologies AG
General discussion on outcome – 25 min

## Slide 3: Agenda
Introduction
UVM Mixed Signal Verification Experience Sharing sessions:
  UVM-MS mixed signal extensions
    Joen Westendorp, NXP Semiconductors
  A-UVM — A Transaction-Oriented UVM-Based Library for Verification of Analog Behavior
    Sebastian Simon, Infineon Technologies AG
General discussion on outcome

## Slide 4: Introduction
UVM is a SystemVerilog base class library that standardizes common functions like testbench class structure, testbench component communication and data automation features, like packaging, copy compare, debug
2009 Accellera voted to establish UVM standard based on OVM2.1.1 developed by Cadence Design Systems and Mentor Graphics.
2011 Accellera approved the 1.0 version of UVM
2014 Accellera released version 1.2 of UVM
2017 IEEE release of UVM LRM as IEEE 1800.2-2017
LRM Language Reference Manual

## Slide 5: Introduction
Goal of this tutorial
  Show current best practices used by different companies
    focus on advantages of practice
    disadvantages/workarounds/future plans, best in light missing STDs/EDA tools
  Discuss audience experience in AMS verification with UVM
  Discuss if creation of an UVM-AMS Accellera working group is something that would be supported by the audience

## Slide 6: Agenda
Introduction
UVM Mixed Signal Verification Experience Sharing sessions:
  UVM-MS mixed signal extensions
    Joen Westendorp, NXP Semiconductors
  A-UVM — A Transaction-Oriented UVM-Based Library for Verification of Analog Behavior
    Sebastian Simon, Infineon Technologies AG
General discussion on outcome

## Slide 7: UVM-MS mixed signal extensions
Joen Westendorp, NXP Semiconductors

## Slide 8: Contents
Introduction
Layers of a verification environment
Rationale
UVM Mixed signal
The analog mixed signal Verification Component
Mixed signal UVC
Required definitions
Questions

## Slide 9: Introduction
Mixed signal integration verification is about functional verification of analog and digital circuits together.
Digital only verification is much more developed and methodical than analog verification
Functional verification of mixed signal circuits is biased to use digital verification methodologies, like UVM
UVM provides a structured and layered verification methodology, however UVM is not the only existing verification methodology
  The UVM layers are not defined to deal with analog signals
This is about extending digital verification environments into the AMS domain, to enable MS verification instead of simulation (use UVC’s).

## Slide 10: VE Layers

## Slide 11: Rationale
Extendibility
  New functionality can be added without changing existing functionality, a new component can be created by deriving it from an existing one
Maintainability
  The architecture is modular and everything is in a logic place, later changes will not affect already existing use models
Configurability
  Functionality can be selected and modified without changing the code, a test bench does not need to be changed when another signal is required

## Slide 12: UVM-Mixed Signal

## Slide 13: AMS Verification component

## Slide 14: Mixes signal UVC

## Slide 15: Advantages of Approach
TBA

## Slide 16: Disadvantages/Workarounds/Future Plans Definitions required
Addition mixed signal verification components
  Meters
  Models
  Primitives
  Transactors
Structure
  Agent
  Agent extension
Interfaces between layers
  Translation from transaction level to the signal layer is well defined through sequences
  Definition of flexible API’s between the physical and signal level layer still needed (also a common interface to connect to 3rd party VIP)

## Slide 17: Questions

## Slide 18: Agenda
Introduction
UVM Mixed Signal Verification Experience Sharing sessions:
  UVM-MS mixed signal extensions
    Joen Westendorp, NXP Semiconductors
  A-UVM — A Transaction-Oriented UVM-Based Library for Verification of Analog Behavior
    Sebastian Simon, Infineon Technologies AG
General discussion on outcome

## Slide 19: A-UVM — A Transaction-Oriented UVM-Based Library for Verification of Analog Behavior
Sebastian Simon
Infineon Technologies AG

## Slide 20: Outline
Motivation
A-UVM: Analog extension to UVM
Application: IGBT driver
Summary
1
2
3
4

## Slide 21: Traditional Analog/Mixed-signal Verification
Mixed-signal top-level verification means …
  … confirming functional correctness with respect to the specification
  … analysing waveforms in the time domain
Traditional analog verification approach has a couple of limitations:
  Directed testing  Critical scenarios might be left out
  No metrics for functional coverage  Are we done?
  Waveforms are often manually inspected  Has to be repeated after each regression
   Error-prone, inefficient and time-consuming!
   We need automation and reusability!

## Slide 22: Automation in the Analog Domain
Frequency
Slewrate
Voltage level
Specification
Automated checks:
Pass?
Fail?
Chart: 
Time
Voltage
Automated Signal Parameter Extraction

## Slide 23: Outline
Motivation
A-UVM: Analog extension to UVM
Application: IGBT driver
Conclusion
1
2
3
4

## Slide 24: A-UVM (Analog-UVM)
A-UVM
Analog transaction
Monitor
trigger
Analog check
Analog/Mixed-Signal Extension to UVM
“Shape” of signals, parameters to describe a shape, with a time duration
UVM
UVM transaction:
signal value
Transaction collected on signal changes or events
Monitor recognizes events to determine the start and end of one transaction
Comparison:
Bit-wise
Comparison of real-value vectors using specific mathematical algorithms
Digital
Analog

## Slide 25: A-UVM: Transaction
Name: sine
Freq: 200kHz
Ampl: 5V
Dur: 5us
Phase: 10°
Input_a =1’b1;
Input_b =1’b0;
A
B
UVM Transaction
A-UVM Transaction

## Slide 26: A-UVM (Analog-UVM)
Sequencer
Monitor
Monitor
DUT
Scoreboard
Test case
Environment
Agent
Agent
Sequence
trans
Trans:
Name: sine
Freq: 200kHz
Ampl: 2V
Dur: 5us
Trans:
Name: sine
Freq: 400kHz
Ampl: 2V
Dur: 5us
trans
trans
Test result
Driver
Sine
algorithm
Sine
algorithm
Sine
algorithm
Trans:
Name: sine
Freq: 200kHz
Ampl: 2V
Dur: 5us

## Slide 27: A-UVM: Driver & Monitor Algorithms
Trans: level, increment, duration
Driver algorithm: sample rate
Trans: level, duration
Driver algorithm: sample rate
Trans: frequency, phase, amplitude, offset, duration
Driver algorithm: sample rate
Trans: signal values, duration
Driver algorithm: sample rate, interpolation mode
Ramp
Sine
Constant
Sampling
Monitor calculates level and increment
Monitor calculates phase frequency, amplitude and offset
Monitor collects one value in one transaction as new level
Monitor samples signal in one transaction using defined sample rate
Driver
Monitor
Trans: real and imaginary values
Driver algorithm: sample rate
Fourier
Monitor samples signal and performs Fourier transformation

## Slide 28: A-UVM: Trigger Mechanism
Start Trigger
Stop Trigger
Cancel Trigger
Level Trigger
Time Trigger
Jump Trigger
Callback Trigger
Recursive Trigger
Event
Transaction
Logic
Real-
time
Example: using crossing of two signals as trigger condition
start
stop

## Slide 29: A-UVM: Stimulus generation
Analog Constrained Random Stimulus
Beta distribution can be used for constrained-random stimulus:
Symmetric vs. asymmetric
Unimodal vs. bimodal
Concave vs. convex
Signal features can randomized based on distributions
  Uniform distribution
  Gaussian distribution
  Beta distribution

## Slide 30: A-UVM: Comparison of Analog Signals
Cosine similarity
Pearson product-moment correlation coefficent
Tanimoto distance
Earth mover’s distance
Comparison of analog waveforms can be performed using different metrics
Provides real value between 0.0 and 1.0 representing degree of similarity
Waveform checks assume lower limit for similarity result  pass/fail

## Slide 31: A-UVM: Analog Coverage Collection
DUT
Analog monitor
Coverage Subscriber
Coverage mapping
Integer-based
Covergroup
Constrained
Random Stimulus
0.0  1
2.4  2
[1.3, 1.6]  3
…
User-defined coverage
Generates analog transactions
ATX
Sampling transaction
Fourier transaction
Basic concept of analog coverage collection:

## Slide 32: A-UVM: Other Features
Plotter/scanner: stores/reads signal information in/from separate files
Sanity check: is applied on the interface to check whether signals exceed a allowed value
More user/project-specific features can be added

## Slide 33: Outline
Motivation
A-UVM: Analog extension to UVM
Application: IGBT driver
Conclusion
1
2
3
4

## Slide 34: Application: IGBT Gate Driver
High-voltage IGBT gate driver designed for motor drives above 5kW (e.g. xEV)
On-chip galvanic insulation via coreless transformer
5V domain
1200V domain
IGBT Driver
xEV Main Inverter

## Slide 35: Application: Specification
Pass?
Fail?
Pass?
Fail?
Pass?
Fail?
Pass?
Fail?
Extracting signal features for two-level turn-on
  Start-trigger for monitoring: posedge of digital input signal
  Algorithm to extract time and voltage parameters based on stable level regions
  Stop-trigger for monitoring: VCC2 level is reached
Two-level turn-on during simulation:

## Slide 36: Application: Configurations
Why spending so much effort on automated feature extraction and automated checking?
  Plateau level and plateau length can be configured via SPI in register fields
  Possible configurations just for turn-on: 7∙246 = 1722
  Narrowed down to interesting scenarios (e.g. extreme cfgs):
    42 conf’s ∙ 5 seeds ∙ 5 turn-on events/conf/seed = 1050 turn-on waveforms (to be checked after each regression)
    Not realizable without automated extraction and checking!

## Slide 37: Outline
Motivation
A-UVM: Analog extension to UVM
Application: IGBT driver
Conclusion
1
2
3
4

## Slide 38: Advantages of Approach
A-UVM Features | Available?
Analog (real-valued) transactions | 
Driving analog constrained-random stimulus | 
Monitoring analog signal features | 
Automated analog checks with pass/fail criteria | 
Similarity analysis of analog signal features | 
Analog Functional Coverage | 

## Slide 39: Disadvantages/Workarounds/Future Plans
TBA

## Slide 40: Agenda
Introduction
UVM Mixed Signal Verification Experience Sharing sessions:
  UVM-MS mixed signal extensions
    Joen Westendorp, NXP Semiconductors
  A-UVM — A Transaction-Oriented UVM-Based Library for Verification of Analog Behavior
    Sebastian Simon, Infineon Technologies AG
General discussion on outcome

## Slide 41: General Discussion on Outcome
To be filled