## Slide 1: Improving the Confidence Level in Functional Safety Tools for ISO26262
Ahmet Cagri Bagbaba, Felipe Augusto Da Silva, Christian Sauer

## Slide 2: Agenda
Introduction
Motivation
Background Information
  Functional Safety and ISO26262
  Fault Injection Simulation
  Automatic Test Pattern Generation
Approach
Results
Conclusion

## Slide 3: Motivation
Functional Safety and analysis of random failures are becoming part of requirements
Tighter integration between functional safety analysis and standard design/verification
Analyse the use cases for all the flow tools
Use redundant methodologies to detect errors in the tool outputs

## Slide 4: Why do we need functional safety?

## Slide 5: Functional Safety – ISO 26262
“Absence of unreasonable risk due to hazard caused by malfunctioning behaviour of electrical and/or electronic systems” (ISO 26262)
Malfunction
What level of safety integrity (risk reduction) is needed?
How much harm can the malfunction cause? (risk)
ASIL (Automotive Safety Integrity Level)
LOW
HIGH
A
D
B
C
Dashboard
Airbag not firing
Braking
ASIL examples for illustration purposes only

## Slide 6: What is Tool Qualification?
ISO 26262 Part 8 “Supporting Processes” covers all aspects of TCL
A Tool Confidence Level is determined based on tool impact (TI) and the tool error detection (TD)
Evaluation of tool outputs is important.

## Slide 7: Flow
Compare two different approaches regarding the results and improve the fault injection simulator’s confidence
Comparison of the results to a different approach increases TCL and provide more optimized fault list

## Slide 8: Fault Injection
Enables to verify the capability of a safety mechanism to recognize failures in design’s functionality by injecting faults into the design
Target system and the possible hardware faults are modelled and simulated by the simulator
Fault Injection simulator needs to know the fault target at which to inject faults
  We enable fault instrumentation on the ports of the cell instances
  Equivalent to using the ATPG semantics

## Slide 9: Fault Analysis by Fault Injection Simulator
Xcelium™ Simulator
Fault list optimization
Fault list generation
Elaboration
Good Simulation
Fault Injection Simulation
fault_target dut... -type sa0+sa1
strobe functional dut.data
strobe checker dut.alarm
Plain Fault List
dut.u0.rst sa0+sa1 faultid=20
dut.u0.sig1 sa0+sa1 faultid=21
dut.u0.sig2 sa0+sa1 faultid=22
dut.u0.sig3 sa0+sa1 faultid=23
Optimized Fault List
dut.u0.rst sa0+sa1 faultid=20
dut.u0.sig1 sa0+sa1 faultid=21 equiv=23
dut.u0.sig2 sa0+sa1 faultid=22 untestable
dut.u0.sig3 sa0+sa1 faultid=23
“Summary” of Annotated Fault List
Stuck-At (0/1) Fault Table
Total #
Untestable 64
Detected 7273
Undetected 1631
Total 8968

## Slide 10: Automatic Test Pattern Generation (ATPG)
Design-for-Test technique
Provide measures to test the manufactured device for coverage and quality
Scan-based test is used
  This replaces D flip-flops with their scan-equivalent flops and serially connects the scan flops into scan chain

## Slide 11: ATPG Flow
Build Model
Build and Verify Fullscan Test Mode
Add Faults
Run ATPG
Create and Commit Logic Test
Write Vectors
Structural Verilog
Report
Analysis
Fault Coverage
Test Vectors

## Slide 12: Approach
Two different comparisons:
  Compare Optimized Fault Lists
  Compare Annotated Fault Lists

## Slide 13: Compare Optimized Fault Lists
Fault list can be generated both by the ATPG tool and fault injection simulator
It is expected that fault injection simulator’s fault optimization achieves the same capabilities as the ATPG tool
Prove that fault injection simulator contains all instrumentation and optimization potential

## Slide 14: Compare Annotated Fault Lists
The fault injection simulator can be used in conjunction with ATPG
Each fault detected by the ATPG tool should be detected by fault injection simulator
Prove that fault injection simulator and the ATPG tool have the same coverage
We need a annotation comparison method

## Slide 15: Annotation Comparison Method
Xcelium Annotation Types | Modus Annotation Types | Check Annotation
Detected | Tested by simulation | PASS
Untestable | Ignored (unclassified) | PASS
Potentially Detected | Tested by implication | PASS
Undetected | Collapsed Tested by simulation | WARNING

## Slide 16: Results: Comparison of optimized fault lists
 | ac97 | aes | dma | total
Nr of instrumented faults | 57226 | 91916 | 66708 | 212850
Nr of optimization differences | 12 | 4 | 76 | 92
Different collapsing approaches of tools have effect on the results
Functionality does not change.
Example: Modus solution does not collapse primary inputs.

## Slide 17: Results: Comparison of annotated fault lists
Design | Xcelium (nr of faults) | Modus (nr of faults) | Check Results
b01 | 230 | 230 | PASS
b02 | 174 | 174 | PASS
b03 | 882 | 882 | PASS
b04 | 2268 | 2268 | PASS
b05 | 2512 | 2512 | PASS
b06 | 274 | 274 | PASS
b07 | 1882 | 1882 | PASS
b08 | 766 | 766 | PASS

## Slide 18: Results Summary
IWLS 2005 and ITC’99 benchmark circuits are used to collect results.
  Analysed for SA0 and SA1 faults
  Analysed for collapsed and untestable faults.
Modus and Xcelium tools generate the same fault lists and same annotation results.

## Slide 19: Conclusion
Functional safety becomes a crucial requirement in the safety critical automotive systems.
This is causing shift in the traditional design flow and pushing ISO 26262 compliance into the traditional EDA tools.
Cadence® offers different technologies capable of generating fault lists.
ATPG from the ModusTM solution can work together with the XceliumTM simulator to create robust and optimized fault injection campaign.

## Slide 20: Acknowledgements

## Slide 21: Thank You Questions?