## Slide 1: UPF Power Models: Empowering the power intent specification
Amit Srivastava and Harsh Chilwal

## Slide 2: Agenda
Introduction
Hierarchical UPF
Challenges with Hierarchical Approach
Power Models
Benefits
Limitations and Future Work
Conclusion

## Slide 3: Introduction
Modern Low Power SoCs integrate many IPs
  With its own power management
  UPF
Current hierarchical UPF methodology is becoming inadequate
  File based
  Instance based, dependent on design hierarchy
New kinds of problems are coming up
  Large number of IPs and instances of IPs
  Code explosion, File management, Tool performance, etc.
A new methodology which empowers the way we write UPF
  Modular UPF
  Based on standard UPF constructs
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA
inst1
SoC
inst2
instN
Power Model
Power Model
inst1
SoC
IP
UPF
inst2
IP
UPF
instN
IP
UPF
SoC
UPF

## Slide 4: Hierarchical UPF
Power Intent is partitioned into separate files
  Typically aligned at the IP boundaries
Files are associated with instances in design hierarchy
Processed for each instances of the IP
  load_upf command
Explicit commands for making connections
  connect_supply_net
  associate_supply_set
  connect_logic_net commands
Enables reuse of power intent for instances of IP
New kinds of challenges in large modern designs
SoC.upf
create_power_domain SoCPD
create_supply_net VDD
load_upf IP.upf –scope inst1
connect_supply_net VDD \
–ports inst1/VDD
load_upf IP.upf –scope inst2
connect_supply_net VDD \
–ports inst2/VDD
...
IP.upf
create_power_domain IPPD
create_supply_port VDD
...
IP.upf
create_power_domain IPPD
create_supply_port VDD
...
IP.upf
create_power_domain IPPD
create_supply_port VDD
...
inst1
SoC
IP
UPF
inst2
IP
UPF
instN
IP
UPF
SoC
UPF

## Slide 5: Code Explosion
Instance based association causes code explosion
  load_upf for each instance
  Supply and logic connections for each supply on the instance
A real problem for large designs
  100s of IPs, 1000s of instances of IPs
Multiplication of UPF code needed for IP integration
More problems in large development environments have UPF files
  Inside deep nested directories
  Having long cryptic names
Functional issues due to incorrect power intent association
load_upf /a/b/c/d/e/upf/sadcls0c4l1p32x10m4b1w0c0p0d0t0s2sdz1rw00.upf
-scope U_sms_wrapper1_int_top/U_sadcls0c4l1p32x10m4b1w0c0p0d0t0s2sdz1rw00
connect_supply_net VDD \
-ports U_sms_wrapper1_int_top/U_sadcls0c4l1p32x10m4b1w0c0p0d0t0s2sdz1rw00/VDD
connect_supply_net VSS \
-ports U_sms_wrapper1_int_top/U_sadcls0c4l1p32x10m4b1w0c0p0d0t0s2sdz1rw00/VSS

## Slide 6: Tcl Scripting
Use Tcl scripting capabilities to reduce code
  Variables, if-else, foreach
Has its own problems
  Readability
  Debuggability
UPF Code becomes more complex
No protection from unintended variable assignments
set mem_instances [find_objects \
-model sadcls…c1p1d1r3s2sdz1rw00 \
-pattern * \
-object_type inst \
-transitive TRUE ]
set mem_upf
"/…/upf/sadcls…t0s2sdz1rw00.upf"
foreach instance $mem_instances {
if {$instance == “...”} { }
load_upf $mem_upf
-scope $instance
connect_supply_net VDD \
-ports $instance/VDD
connect_supply_net VSS \
-ports $instance/VSS
}

## Slide 7: File Management
File based splitting causes additional overhead of file management
Keep track of
  IP vs Power Intent mapping
  IP instance vs Power Intent mapping
  IP version changes
  Location of IP UPF
Library of UPF cant be created
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY

## Slide 8: Tool Performance
Tool suffers performance degradations
  More UPF code results in more processing
Less potential for tool optimizations
  Each instance can potentially have its own power intent
A sample case study on SoC designs from two different customers
Customer Scenarios | No. of Hard Macros | No. of load_upf | Compilation Time with load_upf
Customer #1 | 338 | 18051 | ~13 hrs.
Customer #2 | 12 | 24432 | ~6 hrs.
This Photo by Unknown Author is licensed under CC BY-ND

## Slide 9: Modular UPF A new methodology for UPF Specification

## Slide 10: UPF Power Models
Power Models provide a modular way of writing UPF
  Similar to module/endmodule in SystemVerilog
Power Intent described for logical power model
  Mapped to one or more models
Uses
  begin_power_model/end_power_model
  define_power_model (in UPF 3.1)
Applied to one or more instances of model
  apply_power_model command
PM.upf
begin_power_model SoCPM
create_power_domain SoCPD
create_supply_net VDD
apply_power_model IPPm \
-supply_map { \
IPPD.primary SoCPD.primary
}
...
end_power_model
begin_power_model IPPm
create_power_domain IPPD
create_supply_port VDD
...
end_power_model
apply_power_model IPPm \
-supply_map { \
IPPD.primary SoCPD.primary
}
inst1
SoC
inst2
instN
Power Model
Power Model

## Slide 11: Benefits
Automatic instantiation with single command
Supply and logic connections at the time of instantiation
Inbuilt checks to ensure correct by construct UPF
  Model vs Instance mapping
  Connection consistency
  Protected environment
begin_power_model SRAM_Synch_1Port
-for {
sadcls0c4l1p32x10m4b1w1c1p1d1r3s2sdz1rw00
sadcls0c4l1p32x10m4b1w0c0p0d0t0s2sdz1rw00
}
create_power_domain PDP
create_power_domain PDA_SW -elements {uut} \
-scope uut
# ... Other UPF Commands
end_power_model
# This applies for all instances of
# sadcls0c4l1p32x10m4b1w1c1p1d1r3s2sdz1rw00
# sadcls0c4l1p32x10m4b1w0c0p0d0t0s2sdz1rw00
apply_power_model SRAM_Synch_1Port \
-port_map {{VDD VDD} {VSS VSS}}

## Slide 12: Library of Power Models
Independent of file based mapping
A single power model can represent family of IPs
  -for option to associate multiple IP models
Multiple power models in same file
  Can be used to model a library of power models
# SRAM Library
begin_power_model SRAM_Synch_1Port
-for {
sadcls0c4l1…w1c1p1d1r3s2sdz1rw00
sadcls0c4l1…w0c0p0d0t0s2sdz1rw00
}
create_power_domain PDP
# ... Other UPF Commands
end_power_model
begin_power_model SRAM_Synch_2Port
-for {sadrls0c4l2…w1c1p1d1r1s2z1rw00}
create_power_domain PDP
# ... Other UPF Commands
end_power_model

## Slide 13: Tool Performance
Power models help in improving tool performance
Model based representation and hence can be reused for each instance of model
  Tools can perform several optimizations
Case study: Comparison with load_upf on Customer designs
Customer Scenarios | No. of Hard Macros | No. of load_upf | No of apply_power_model commands | Compilation Time with load_upf | Compilation Time with apply_power_model
Customer #1 | 338 | 18051 | 710 | ~13 hrs. | ~6.5 hrs.
Customer #2 | 12 | 24432 | 122 | ~6 hrs. | ~3 hrs.
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 14: IP Variations
Can have minor variations
  Operating voltages
Parameterize using variables
load_upf in UPF 3.0 supports –parameters
  Requires instance wise specification of parameters
  Error prone
Power models allow parameters to be created
  add_parameter command
Overridden by apply_power_model –parameters option
begin_power_model IP
add_parameter NORMAL_VOLT -default 1.0
create_power_domain PDTop
# ... UPF commands
add_port_state VDDA
-state "NORMAL $NORMAL_VOLT"
-state {OFF off}
# ... UPF commands
end_power_model
# SubSystem1.upf
create_power_domain PDSubSys1
apply_power_model IP
-parameters {
{NORMAL_VOLT 1.0}
}
# SubSystem2.upf
create_power_domain PDSubSys2
apply_power_model IP
-parameters {
{NORMAL_VOLT 1.2}
}

## Slide 15: Limitations in UPF 3.0
Protected Environment
  begin_power_model/end_power_model do not provide protection from global variables
  Replaced by define_power_model in UPF 3.1
Supply and Logic Port Connections
  No ability to connect supply nets and logic nets
  New option –port_map added in UPF 3.1
Use of Tcl parameters
  add_parameter restricted to System level models
  UPF 3.1 extends add_parameter to allow Tcl parameters
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 16: Future Extensions
Implicit instantiation
  Automatically instantiate power models for
    Hard macros
    Top design
Updates to power model
  No ability to directly update the intent of power model
Mantis filed to request enhancements in UPF 4.0.

## Slide 17: Empowering Power Intent Specification
Power models provide a modular based methodology of UPF
Works seamlessly with hierarchical based methodology for modern designs
Uses inbuilt UPF semantics to eliminate human errors in UPF specification
Empowers
  Users
    Minimal code
    Self checking
  Tools
    Improved performance
  Library vendors
    UPF library similar to liberty library
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 18: References
References
  IEEE Standard for Design and Verification of Low-Power, Energy-Aware Electronic Systems," in IEEE Std 1801-2015 (Revision of IEEE Std 1801-2013) , vol., no., pp.1-515, March 25 2016
  Mohit Jain, Amit Singh, JSSS Bharath, Amit Srivastava, Bharti Jain , “Power Aware Models: Overcoming barriers in Power Aware Simulation”, DVCon Europe 2014.
  Tim Kogel, “Applying UPF 3.0 for Early, System-level Power Analysis of SoCs with DDR Memories”, DVCON EUROPE 2016.
  VCS Native Low Power with MVSIM, https://www.synopsys.com/verification/simulation/vcs-with-mvsim.htm

## Slide 19: Questions
Thank You