## Slide 1: Hybrid Flow: A smart methodology to migrate from traditional Low Power Methodology
Rohit Kumar Sinha, Intel India
Prashanth N, Intel India

## Slide 2: Agenda
Low Power Overview
Low Power Optimization in Design
Intel Client Low Power Methodologies
Motivation : Traditional Vs Proposed
Power Intent Body
Introduction to hybrid Methodology
Challenges in Hybrid Flow
Advantages of Hybrid Methodology

## Slide 3: Low Power
Power Management is Critical Today
Driving for finer process technology
  Smaller, lighter products
  Longer battery life
  More functionality
Dynamic power
  Signal switching consumes energy
  Was the major contributor to power consumption
Static power
  Static leakage can consume 50% of power!
  Now the major concern for power optimization

## Slide 4: Motivation :Traditional Vs Proposed
Complexity of the Design
IP Sourced from multiple vendor – Internal, External & Hard IPs.
Need of the hour is Abstraction
Physical Design Limitation
Multiple Flows for Functional Verification vs Implementation
Large Number of Power and Voltage Domains
Adoption of new feature of latest power intent

## Slide 5: Power Intent Body
Top level domain definition
Supply Interfaces (creating supply sets, ports, nets)
Connecting Supplies
Load and integrate sub-components of Units or IPs
Load the power intent bodies of sub-systems or partitions
Defining the level shifter strategies, isolation strategies & retention control strategies
Defining the set related supply nets for ports and pins if it differs from the default
The PST describes all the valid combinations of voltage states that can exist in the design
Top Interface
Defining low power strategies
Loading of UPFs
Defining SRSNs strategies
Defining PSTs
add_power_state "VCCSA" -state "ps_VCCSA_LV" "-supply_expr \{power == `\{FULL_ON,0.65\}\} -simstate NORMAL
set_isolation punit_vccsa_vccstl_iso_dummy \
-domain "vccstl_domain_merge" \
-isolation_supply_set "VCCSTL" \
-isolation_signal "punit_wrap/punit/ptpcbclk/ptpcbclk_soft_supply" \
-isolation_sense "low" \
-location "self" \
-elements [list \ "punit_wrap/punit/ptpcbclk/PllXclkSyncFnn4H" \
set_port_attributes -ports [join $iov_clamp_value_1_elements] -clamp_value
create_power_domain "vccsa_domain_merge" \
-supply {extra_supplies_1 VCCSA} \
-supply {extra_supplies_2 VCCSTL}
create_supply_net "vcc_in" create_supply_port -direction "in" "vcc_in"
connect_supply_net "vcc_in" -ports "vcc_in" create_supply_net "vcc_out"

## Slide 6: Introduction to Hybrid Methodology
Partition with merged UPF
Merge Flow (All the power domains are merged to 1. All the SIPs are merged into single domain
Unit Level- U11, U12…U1n. Units are wrapper around IPs.
SoC Design
Soft IPs
Soft IPs comes as a synthesizable module in hardware description languages (HDL) such as SystemVerilog or VHDL. Ex – CPU, Power Control Module etc
Hard IPs is a predesigned layout with all power management functionality built into the IP itself. Ex - DDR PHYs, USB PHYs, PLLs etc.
Partition with hierarchical and UPF2.x
Hard IPs (UPFs + Libs
Hard IPs (UPF +Libs)
Soft IPs.
Unit Level- U21, U22…U2n. Units are wrapper around IPs.
UPF2.x
UPF1.0
Hierarchical UPF2.x power intent is used for FV and implementation Flow
Hier. Partition UPF
Static Checker
Spyglass Low Power
Functional Verification
VCS Native Low Power
Emulation
ZEBU
Synthesis
Design Compiler
ICC2

## Slide 7: Intel’s SoC Design Integration Flow
IP Level
(UPFs, Libs)
Developed power intent
Unit Level
(Load UPFs for SIPs & HIPs)
UPF Owner are supposed to load the unit UPFs and build the hierarchal power intent.
Partition Level
Partition Level has 2 flavors of power intent
Collage integrates IP UPFs into FE model
SoC Level
(Different SoC Flows are used for Functional Verification & Implementation
Quality sign off for all stages
Static, functional verification, emulation, implementation
Unit is essentially a wrapper around for SoC usage
Auto generation of merged partition UPFs for the implementation
Hierarchical flow is mainly used for the functional verification flow
SOC designs are verified with 2 different methodology because of the traditional flow limitation. Functional verification and emulation flow is build for SoC Level whereas Implementation Flow quality is being checked at partition level and SoC Level
Low Power Specs are defined as Micro Power Architect and it included top interfaces, partitions level interfaces, crossing table & bump details.

## Slide 8: Hybrid Flow Implementation
Block Type | Cell count | Number of power domains
Power management | ~48000 | 3
Legacy | ~24000 | 3
Fabric | ~87000 | 3
IOP | ~17000 | 3
MC Main | ~4000 | 3
Client SoC with more than 1billion gates design
SoC Contains 34 partitions with memories, power management, PCI, CPU, Display blocks
5 different partition design blocks
Multiple Flows for Functional Verification vs Implementation
Large Number of Power and Voltage Domains
Adoption of new feature of latest power intent

## Slide 9: Challenges of Hybrid Methodology
set_design_atribute -elements <list of elements> -attribute SNPS_treat_as_unconnected TRUE
In Source-Sink isolation strategy, “HETEROGENEOUS_FANOUTS” Warning (Isolation is skipped).
Here same signal out1 is given as input to PD2 block and also for PD3 block ..
Sinks related to PD2 are not real sinks and sink PD3 is a real one .Would like to exclude sinks related to PD2.

## Slide 10: Challenges in Hybrid Flow Implementation
Terminal boundary issue:
Isolation cell with source and sink strategy got matched but isolation cell is not placed due to crossover contain a wire
which belongs to terminal boundary
But due to terminal boundary set on BLK1 element and signal is crossing via wire which is used in BLK1 is
breaking this connection .
Attribute used: set_design_attributes -elements {soc_tb/soc/par_punit/punit_wrap/punit/assert_xcheck_punit
soc_tb/soc/par_punit/punit_wrap/punit/assert_ifc_stability_check_punit} -attribute SNPS_treat_as_unconnected TRUE

## Slide 11: Physical Design challenges…
Power switch insertion issues
Shadow domain solution for optimization

## Slide 12: Physical Design Challenges..
IC Compiler 2 demands matching between states in top level PST and sub hierarchy PST. The solution for this is to disable lower level PST.
Fig. 3.5 Top level PST
Fig 3.6 Missing 1.1 V modeling

## Slide 13: Physical Design challenges
Missing supply states issue: A group of hierarchical PDs in the same VA will share same primary supplies but if there is a mismatch in secondary domains, as long as at least one domain contains the required supply as available supply, tool can use the hierarchy of the domain to put the cell anywhere in the VA physical shape.

## Slide 14: Advantages of Moving to Hybrid flow
Hierarchical methodology with hybrid flow supports partitioning, parallel development, and reuse.
The UPF complexity is very much reduced.
Supply sets provides an abstraction and allows designers to define their power intent without having to create the actual supply nets
Usage of hierarchical flows at all the stages of design flow eliminates the usage of two different UPFs.
Advantages of add_power_state
The usage of set_design_attribute allows the propagation of power information to the lower levels of design hierarchy

## Slide 15: Questions
Finalize slide set with questions slide