## Slide 1: Characterizing RF Wireless Receivers Performance in UVM Environment
Ahmed Nasr
Mohammed T. Abdel-Hafez
Salwa Elqassas

## Slide 2: RF Wireless is coming
Grow rapidly.
Become essential to our lives.
Rising IoT drives wireless to be bigger

## Slide 3: Wireless Communication Challenges
Thermal Noise
Interference Signal
Multipath Fading Interference

## Slide 4: Wireless Communication Challenges
Reduced Signal Noise
Transmitter
Receiver
Interfere Signal
AWGN
Original Signal

## Slide 5: Characterizing Wireless Receiver
RF wireless receiver performance characterized by:
  Receiver Sensitivity
  Interference Performance
Terminologies:
  Additive White Gaussian Noise (AWGN)
  Packet Error Rate (PER)
  Bit Error Rate (BER)
  Carrier to Interference Ratio (C/I)
  Signal to Noise Ratio (SNR)

## Slide 6: Receiver Sensitivity
Thermal noise in the wireless medium produces BER into transmitted packets.
Wireless channel with thermal noise can be modelled as AWGN channel.
Receiver input level for certain BER is the receiver sensitivity.

## Slide 7: Interference Performance
Interferers signal are messages that are sent in-band or around the band original message are transmitted.
C/I defines power ratio between original signal and the interferer.
Receiver sensitivity for each C/I determine receiver interference performance.

## Slide 8: Characterizing RF receiver in UVM environment
Make use of Functional simulation to characterize RF receivers.
Model AWGN to calculate receiver sensitivity.
Mimic Interferer effect on the transmitted signal

## Slide 9: AWGN Modelling
A UVM-SV agent is implemented to model the transfer function of the AWGN.
Implementation by SystemC language through DPI.
The Agent is driving virtual interface bound to internal signals in the receiver part of the DUT.

## Slide 10: AWGN Modelling (Cont’d)
Typical RX chain usually starts with LNA block.
Adding the AWGN to the LNA requires sampling with very high frequency.
Our proposals to inject the noise after the down-conversion mixer.
Operating in lower frequency saves tangible time in simulations.

## Slide 11: Injecting AWGN in the RX chain
AWGN1
AWGN2
DUT RX CHAIN

## Slide 12: Injecting AWGN in the RX chain(Cont’d)
AWGN Agent generates two uncorrelated AWGN vectors.
Each vector will be injected to one input of the complex filter.
AWGN Agent has a configuration to control noise power and therefore SNR.
Up-Conversion is done for both inputs and so I and Q has no relation.

## Slide 13: UVM Environment with AWGN Agent

## Slide 14: BER/PER Calculations
Using UVM reporting mechanism to report transmitted and received packets.
BER/PER calculated through scripts that analyze simulation reports.
Sweeping different SNR values to calculate corresponding BER/PER
Relation between sensitivity and SNR is :
  𝑆𝑁𝑅 = 𝑆𝑒𝑛𝑠𝑖𝑡𝑖𝑣𝑖𝑡𝑦 − ( 𝐾𝑇𝐵 + 𝑁𝐹)
  Where 𝐾𝑇𝐵 is the thermal noise power in the receiver and 𝑁𝐹 is the noise figure.

## Slide 15: Simulation Management
Measuring PER requires simulating with large number of packets.
Simulating with these numbers take a lot of time.
Our approach proposes dividing the packets on number of parallel simulations.
External scripts process reports from these simulation to generate results.

## Slide 16: Interferer Injection
Another instance of the DUT is instantiated to mimic Interferer device.
This instance is configured to transmit on different channels around the original DUT’s frequency channel.
The power of the transmitted data by the interferer instance define the C/I.
This interferer power configured by a test configuration.

## Slide 17: UVM Environment with the Interferer DUT

## Slide 18: Lab Results vs Simulation Results
System | SNRLab (dB) – SNRSim (dB) | SensitivityLab (dB) – SensitivitySim (dB)
System 1 | 0.4 | 0.4
System 2 | 0.2 | 0.2
For two wireless systems with the same BER difference is :

## Slide 19: Questions