## Slide 1: Formal Verification of a Highly Configurable DDR Controller IP
Sumit Neb – Synopsys Inc.
Chirag Agarwal, Deepak K. Gupta, Roger Sabbagh – Oski Technology

## Slide 2: Agenda
Introduction to XPI
XPI Formal Sign-Off
Conclusions and Next Steps

## Slide 3: Synopsys DesignWare Cores DDR Verification
Comprehensive DDR IP including protocol, memory controller and PHY
Benefits
  Development cost, project risk, time-to-market
Highly configurable
  Allows trade-offs between performance, power and area
Verification challenge
  Too many possible configurations to practically test
Notes: Introduce the DW DDR core
Explaing the high level benefits of IP in general
Explain about configurability of IP in general
Introduce the verification challenge for configurable IP

## Slide 4: AMBA® AXI® Port Interface (XPI) Controller
XPI main functions
  Convert AXI bursts into read/write requests to the Port Arbiter
  Convert replies from the DDRC into AXI responses
Independent Read and Write channels
  Write address and data
  Write response
  Read address
  Read data response
Notes: Introduce XPI

## Slide 5: XPI Functionality
Converts the AXI rd/wr commands into proprietary rd/wr commands
Split/ merge the AXI wdata beats based on the beat size at proprietary interface
Similarly, split/ merge the rdata beats from proprietary interface based on AXI beat size
Reorder the rdata coming from proprietary interface
8B
8B
4B
4B
4B
4B
XPI
AXI interface (beat size 8B)
Proprietary interface (beat size 4B)
4B
4B
4B
4B
8B
8B
Out-of-order rdata beats
AXI wdata beats
Split wdata beats
AXI rdata beats
 |  | AXI transaction |  |  | Proprietary transaction (beat size 4B) |  |  | 
1) Split | AXI beat size 8B | 8B | 8B |  | 4B | 4B | 4B | 4B
2) Merge | AXI beat size 2B | 2B | 2B |  | 4B |  |  | 
Notes: Introduce XPI

## Slide 6: XPI Configurability
HW Parameters
  >100 parameters
  Controlling features, such as:
    Address and Data bus widths
    Burst lengths
    Command support
    Parity / ECC protection
    Dual channel support
    Interleaving
    Upsizing and downsizing
  Define most common HW configs for formal verification
SW Configuration Registers
  >60 config registers
  Controlling modes, such as:
    Burst length expansion mode
    Pagematch
    SDRAM burst length
    Read reorder buffer
    OCCAP
    Port enable
    On chip parity
  Define legal range of values for each HW config
Notes: Describe XPI configurability
Explain the challenge to verify all possible combinations of HW and SW configs

## Slide 7: XPI Legal SW Configurations
Register Name | Size | Legal values for HW Config0 | # Combinations for HW Config 0
reg_0 | 4 | 4, 2 | 2
reg_1 | 2 | 0, 1 | 2
reg_2 | 1 | 0, 1 | 2
reg_3 | 4 | 0 to 7 | 8
reg_4 | 5 | 0 to 7 | 8
reg_5 | 1 | 0, 1 | 2
reg_6 | 1 | 0, 1 | 2
reg_7 | 1 | 0, 1 | 2
reg_8 | 1 | 0 | 1
reg_9 | 1 | 0, 1 | 2
reg_10 | 3 | 0 | 1
reg_11 | 1 | 0, 1 | 2
reg_12 | 8 | 0 to 8'hFF | 256
reg_13 | 8 | 0 to 8'hFF | 256
reg_14 | 1 | 0 to 3 | 4
reg_15 | 1 | 0, 1 | 2
reg_16 | 1 | 0 to 3 | 4
…
Define the legal range of SW configs for a given HW config
Total number of legal combinations: 1x1016
Challenge to exhaustively test
reg_58 | 2 | 0, 1, 2 | 3
reg_59 | 2 | 0, 1, 2 | 3
reg_60 | 2 | 2 | 1
reg_61 | 2 | 0, 1 | 2
reg_62 | 2 | 0, 1 | 2
reg_63 | 2 | 0, 1 | 2
…
…
…
Notes: The number of combinations of SW config register settings is too large to test without formal

## Slide 8: Agenda
Introduction to XPI
XPI Formal Sign-Off
Conclusions and Next Steps

## Slide 9: Oski Formal Sign-Off Methodology
Quality of formal results depends on all four “Cs”
Design Under Test
(DUT)
Constraints
End-to-End
Checkers
Coverage
(Code and Functional)
Complexity
(Abstraction Models)
Design Under Test
(DUT)
Notes: Formal is not just for bug hunting anymore
Formal sign-off can replace simulation for complex blocks

## Slide 10: Decomposition for Formal Verification
XPI partitioned along natural boundaries
  Write Path
  Read Control Path
  Read Data Path
Configurable FV testbench developed for each partition

## Slide 11: XPI End-to-End Requirements
Data Integrity
  Data shall not be dropped, duplicated, corrupted or generated spuriously
  For Read Address/Data, Write Address/Data/Response
  Test all combinations of bus widths, burst sizes, etc.
Forward Progress
  Verify absence of deadlock, livelock or starvation
  A Valid signal input shall receive a corresponding Ready output within a bounded number of clock cycles, excluding cycles with backpressure
  A transaction accepted at the input shall be transferred to the output within a bounded number of clock cycles, excluding cycles with backpressure
Notes: What are the main verification goals / worry cases?

## Slide 12: Configurability of Checkers
HW Configurability
  Parameters and macros are defined for each formal run
  Exhaustively test each configuration in a single formal run
Examples:
  Features disabled
  Data bus widths
SW Configurability
  SW control registers made cutpoints in formal
  Explore all legal combinations in a single formal run
Examples:
  block_en
  burst_length

## Slide 13: Challenge of Building the End-to-End Checks
Supporting the large number of SW and HW configurations
Complex transfer function to be modelled
  Split/merge the data based on beat size
  Out of order RDATA
  Converting the AXI transactions with WRAP burst type
    Wrap bursts converted to 2 incremental bursts

## Slide 14: Constraints
Constraints restrict input space to legal range
Over-Constraint
Under-Constraint
Total Input Space
Legal Input Space
Constraints

## Slide 15: XPI Interface Constraints

## Slide 16: Coverage
Formal coverage is part of the sign-off criteria
  Grades the quality of the other 3 Cs
Types:
  Controllability coverage
    How much of the design is reached by formal?
  Observability coverage
    How much of the design is checked by formal?
DUT

DUT

## Slide 17: Formal Controllability Coverage
Finds dead code
  Proven unreachable with no constraints
Grades constraints
  Proven unreachable due to constraints
  Can indicate overconstraints
Grades complexity
  Bounded proofs
Formal Engines
DUT

## Slide 18: Bounded Proof Coverage
Bounded proofs are exhaustive analysis to N-cycles
Deepest coverage point (C)
  For C > N, cannot sign-off
  All cases not covered by bounded proof
  Need to overcome complexity barriers
R
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
2
. . .
. . .
. . .
N
Proof Depth
C

## Slide 19: Formal Observability Coverage
Grades completeness of checkers
  Quantity, quality
Cone-of-influence (COI) coverage
  First approximation
  Quick feedback
Formal engine coverage
  More accurate than COI
  Collected during the formal run
Checker
Cone-of-
Influence
Formal
Engine

## Slide 20: XPI HW Config0 Coverage Metrics
Coverage | Total Points [T] | Deadcode [D] | Covered [C] | Uncovered | Inconclusive | % Coverage [%C/(T-D)]
Line | 1,223 | 58 | 1,163 | 0 | 2 | 99.8
Condition | 809 | 99 | 693 | 1 | 16 | 97.6
Coverage | Total Points | In COI | Out of COI | % Coverage
Cone-of-Influence (COI) | 283 | 183 | 100 | 64.7
Formal Engine (FE) | 283 | 170 | 113 | 60.0
18 Deep coverage points not reached
100 coverage points not used in this config
Controllability Coverage
Observability Coverage
113-100 = 13 points not checked by formal engines

1 coverage point not reachable in this config


## Slide 21: Complexity
Results of analysis of the unreached and unchecked coverage points:
Deep FIFOs
  Unable to cover full range of read/write pointer counters
Token manager
  Highest available token value is released first
  Unable to cover lower range of token values

## Slide 22: Reset Value Abstraction
Addition of allowed, legal states at reset
Reduces required proof depth
R
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
2
8191
753
255
. . .
. . .
. . .
Deep state: FIFO full
R
R
R
Apply to:
FIFO pointer counters
Token manager status register
Deep state: Token 0 released

## Slide 23: XPI HW Config0 Coverage with Abstraction Models
Coverage | Total Points [T] | Deadcode [D] | Covered [C] | Uncovered | Inconclusive | % Coverage [%C/(T-D)]
Line | 1,223 | 58 | 1,165 | 0 | 0 | 100
Condition | 809 | 99 | 709 | 1 | 0 | 99.9
Coverage | Total Points | In COI | Out of COI | % Coverage
Cone-of-Influence (COI) | 283 | 183 | 100 | 64.7
Formal Engine (FE) | 283 | 183 | 100 | 64.7
Controllability Coverage
Observability Coverage


All coverage points checked in this config
All coverage points reached in this cofig

## Slide 24: XPI Formal Verification Sign-Off
Developed configurable formal testbench
  Coded >70 formal checkers
  Enables multiple HW configurations to be tested
  Supports the full range of legal SW configurations for each HW config
Sign-off criteria included:
  FV plan review – list of checkers and constraints
  Formal coverage metrics
  Negative testing
  FV testbench code reviews

## Slide 25: Agenda
Introduction to XPI
XPI Formal Sign-Off
Conclusions and Next Steps

## Slide 26: Conclusions
Verification challenge for highly configurable IP designs
Formal sign-off increases confidence
  Explores all possible SW configs in a single run
  Configurable formal testbench tests multiple hardware configurations
Formal coverage grades checkers, constraints and complexity

## Slide 27: Future Directions
XPI formal verification testbench enhancements
  Extend to support additional HW configs
  Support corresponding legal range of SW configs
Formal coverage closure for each additional HW config
Extend formal coverage with mutation coverage

## Slide 28: Thank you! Questions