## Slide 1: Increasing Efficiency and Reuse in Modeling SystemC/TLM IPs Targeting Virtual Prototypes for Software Development
David Spieker, Thomas Schuster, Rafael Zuralski, Christian Sauer

## Slide 2
Specifications Hardware/Firmware Fab
Silicon
Software
Chip Proof
System Proof
Historical approach (sequential development)
Early Chip Proof
Specifications Hardware/Firmware Fab
Software
System Proof
TLM-based approach (concurrent development)
TLM Model
Chip Proof
Silicon
Why TLM?

## Slide 3: Current problems in Virtual Prototyping
Lack of appropriate simulation IP
Majority of design IPs only available on register-transfer-level (RTL)
Additional development time for missing TLMs
TLM design goal: High abstraction level to enable software execution
  Boot an operating system
  Load appropriate drivers

## Slide 4: Outline
Modeling approach and creation flow
Module skeleton and infrastructure
Protocol example: USB
Results and conclusion

## Slide 5
General
SystemC/TLM2.0 models
Vendor and tool independent code
Style
Loosely-timed
Fast blocking communication
Temporal decoupling
Direct memory interfaces (DMI)
Interfaces
Data interface based on TLM2.0 sockets
Signal interfaces (reset, irq) modeled using ‚tlm_wire‘
Initiator and target interfaces using TLM2.0 generic payload
Client-side payload carries bit-true data
All payload extensions ignorable
Modeling approach

## Slide 6
Specification
IP-XACT
TLM creation / tlmgen
RTL creation
Manual or automated model creation
...
SystemC model bare-bone
TLM target socket
Register set impl.
RTL
TLM
One common source as interface specification!
Basic register access testbench
Model creation

## Slide 7
IP | Bus IF (TLM) | IO interfaces (TLM) | Comments
lpddr4 | slave | Memory model included | 
pcie | slave + master | Back to back | 
mipi_csi2rx | slave | Read from stream | Pixel generator
mipi_csi2tx | slave | Write to stream | Pixel consumer
mipi_dsi | slave | Write to stream | Pixel generator
usbssp | slave + master | Back to back | 
edp | slave | Write to stream | Pixel generator
i3c | slave | Slave interface included | 
ufs_host | slave + master | Back to back with UFS Dev | 
ufs_card | - | Back to back with UFS Host | Only IO interface
Amber IP models

## Slide 8: Outline
Modeling approach and creation flow
Module skeleton and infrastructure
  Bare-bone structure
  Register implementaion and debugging
  Loggin
  CCI parameters
  Factory framework
Protocol example: USB
Results and conclusion

## Slide 9
Automatically generated module skeleton
  Whole register set as specified by IP-XACT
  Internal register bus
  TLM target socket for register access
Common infrastructure
  CCI parameters
  Logging mechanism
Protocol and Data ports (TLM sockets)
Signalling interface (TLM wires)
Module
Register bus
tlm_utils::simple_initiator_socket
tlm_utils::simple_target_socket
tlm_wire_in
tlm_wire_out
Data Port
b_transport
dbg_transport
store_data
fetch_data
r/w
Data interface
Bit-true protocol interface
Logging/reporting
Analysis interface
tlm_analysis_port
Protocol Port
b_transport
dbg_transport
transfer_data
Register Port
b_transport
dbg_transport
Signal Port
register_handler
trigger_signal
Signal interface
Behavior
CCI parameters
Control Register Bank
module registers
reg_0 ...
Generic model bare-bone

## Slide 10
Using ‘sc_register’ library containing:
  A register class (sc_register)
  A register field class (sc_register_field)
  A register bank class (sc_register_bank)
Supports access rights masks
Hierarchy automatically created by TLM interface generator (tlmgen)
sc_register_bank
...
sc_register
sc_register_field
sc_register_field
...
sc_register
sc_register_field
sc_register_field
...
Register implementation

## Slide 11
Register Viewer
Hierarchical view of:
  Register banks
  Registers
  Register fields
Possible to set values during simulation
Register debugging

## Slide 12
All Amber IPs use common logging facility
Unifies different modules‘ output
Configurable via CCI (coming up next)
Base class that must be inherited
Log Levels
SC_NONE
SC_LOW
SC_MEDIUM
SC_HIGH
SC_FULL
SC_DEBUG
log_DEBUG()() << “This is a debugging message“;
log_MEDIUM()() << “This has a higher importance“;
Logging facility

## Slide 13: Configuration, Control and Inspection (CCI)
Library for exchange of information between SystemC models and tools
All Amber IPs support configuring model‘s behavior with CCI
For example:
  Latency for register access
  Memory read/write latencies
  Module‘s operation mode
  Logging verbosity

## Slide 14: Configuration, Control and Inspection (CCI) ctd’
// file param.conf
module_0 {
!parameters {
verbosity "SC_DEBUG"
bus_master.verbosity "SC_DEBUG"
link_master.verbosity "SC_DEBUG"
link_slave.verbosity "SC_DEBUG"
ering_manager.verbosity "SC_DEBUG"
tring_manager.verbosity "SC_DEBUG"
cring_manager.verbosity "SC_DEBUG"
}
}
GUI for parameter introspection and manipulation

## Slide 15: Factory framework
Factory pattern for quick instantiation of whole virtual platforms
Can instantiate any sc_object that was registered before
Can automatically bind ports
Configurable via text files
static sc_object* create_object(
const std::string& type_name,
const std::string& inst_name,
const char *init_val = NULL
);
sc_object* obj =
create_object(„tlm_wire_in“, „w1“);

## Slide 16: Outline
Modeling approach and creation flow
Module skeleton and infrastructure
Protocol example: USB
  General structure
  Module: USBSSP/xHCI
Results and conclusion

## Slide 17: Behavior Implementation
Generated base class
Register set implementation
Register bus
TLM2.0 target socket
Behavior class
Additional TLM2.0 sockets for
  System memory access
  Application-specific communication protocols
Signal interface
Generated base class
Class with application-specific behavior
Module‘s top-level class

## Slide 18: Protocol example: USB/xHCI
USB as polled protocol
Blocking transport sufficient
Small set of threads
  Transfer management
  Command Ring management
  USB Data transfer
USBSSP
reg_in
tlm_utils::simple_initiator_socket
tlm_utils::simple_target_socket
tlm_wire_in
tlm_wire_out
Control Register Bank
Register Port
b_transport
dbg_transport
USBSSP registers
HCIVERSION_CAPLENGTH ...
r/w
bus_out
irq_out
usb_data_in
usb_data_out
reset_in
USB Data Transfer
b_transport_usb
encode/decode data packets
trigger event generation
Event Ring Mgmt.
reporting to sw
State Control
RESET, HALTED, RUNNING
Command Ring Mgmt.
command request handling
queue filled by sw
Command Ring Mgmt.
reporting to sw
Command Ring Mgmt.
reporting to sw
Transfer Ring Mgmt.
transfer request handling
per endpoint

## Slide 19: Outline
Modeling approach and creation flow
Module skeleton and infrastructure
Protocol example: USB
Results and conclusion

## Slide 20: Results
IP model | Lines of Code |  |  | 
 | complete | generated | manual | manual quota
USB | 45977 | 43335 | 2642 | 5.75%
PCIe | 79638 | 74773 | 4865 | 6.11%
MIPI CSI2RX | 5225 | 4289 | 936 | 17.91%
MIPI CSI2TX | 4428 | 3867 | 561 | 12.67%
MIPI DSI | 7339 | 6590 | 749 | 10.21%
LPDDR4 | 20413 | 19214 | 1199 | 5.87%
SD4HC | 6840 | 5268 | 1572 | 22.98%
High extent of automatically created code
Manual code quota of 11.6% on average

## Slide 21: Conclusion
Virtual System Prototype
SystemC
TLM
Amber IPs
sc_register
TLM wire
Logging
Factory framework / manual instantiation

## Slide 22: Conclusion
Achievements
Availability of common controller IPs in TLM LT modeling style
Common TLM IP infrastructure
Automated model generation flow
Early availability of target platform for software/firmware development
Virtual System Prototype
SystemC
TLM
Amber IPs
sc_register
TLM wire
Logging
Factory framework / manual instantiation

## Slide 23: Questions