## Slide 1: Protocol verification of an IEEE 802.3bw PHY
Joen Westendorp, NXP Semiconductors

## Slide 2: Contents
Introduction
Requirements
UVM-mixed signal
Analog/mixed signal VC
Mixed signal verification library
Protocol UVC
Application to automotive ethernet

## Slide 3: Introduction - Automotive ethernet

## Slide 4: Introduction - Verification challenges
Above all, we need verification instead of simulation
An analog/mixed signal verification approach, combined with state of the art digital verification methodologies is required
Functional coverage needs to be collected at all abstraction levels, ranging from the transaction layer to the physical layer
Physical signals needs to be represented with electrical signals due to superposition of symbols in bidirectional communication between the PHY’s

## Slide 5: Requirements
From state of the art digital verification methodology:
  Configuration
  Extendibility
  Maintainability
For digital, this is offered by the UVM libraries. The need for a similar library targeting A/MS verification is recognized
Verification components (VC’s) need to be supplied. They contain knowledge about verification targets, which can be easily transferred over the team

## Slide 6: UVM-Mixed signal
Layering and components
  Transaction level, contains properties of analog signals
    Sequencer
    Scoreboard, checks specifications
  Signal level, contains a pin level abstraction of analog signals
    Agent
      driver
      monitor
  Physical level, contains waveforms described by (a subset of) physical quantities
    Analog/mixed signal agent extension
      source
      probe
      meter(s)

## Slide 7: Analog/mixed signal VC
Built with an in-house mixed signal verification library
API defined for:
  Connect the mixed signal agent extension to the UVM environment
  Sequence items
  Configuration
Structure defined to:
  Instantiate a model for data pre-/post-processing
  Instantiate AMS primitives like sources and samplers

## Slide 8: Analog/mixed signal VC

## Slide 9: Mixed signal verification library
To facilitate MS-UVC creation, a library has been developed which extends the UVM library.
Analog waveforms can only be generated in modules, not in classes
SystemVerilog packages are used to go from the module into classes, the package is called an adapter
The source and probe components in the adapter override the driver and monitor components in the UVM environment
An API is provided by the adapter, this API is used in the module to access the UVM environment
The run phase is implemented in the module, forwarding the sequence items to the instantiated AMS sources and samplers (it can see the interface to these modules)
This gives the flexibility to extend the verification environment into the module and generate analog (physical) signal

## Slide 10: Protocol UVC
The mixed signal agent extension extends existing VIP’s
The source and probe classes in the adapter uses ‘mix-in’ constructs to be generic, any driver or monitor can be inherited and overridden
A transactor component needs to be used to make a translation in sequence items from a higher layer to a lower layer
The transactor can be inserted in the verification environment as a combination of a driver and a sequencer, a factory override is used to change the original component in the verification environment

## Slide 11: Protocol UVC

## Slide 12: Application
The PCS layer is handled by an existing VIP, covering the digital part of the UVC (signal layer) and using its cover groups
The PMA layer (physical layer) is handled by the mixed signal agent extension where clock recovery etc. are implemented
Required models in the mixed signal agent extension:
  Hybrid
  Clock recovery
  TX/RX block
  And cover groups in a separate uvm_subscriber

## Slide 13: Application
transaction level
signal level
physical level

## Slide 14: Results
Eye diagram obtained from a simulation, real-time processed through Matlab

## Slide 15: Conclusions
An A/MS library similar to UVM enables us to build components which extend existing UVM VIP to create mixed signal UVC’s
Transactor components make the translation of abstraction levels between protocol layers. The translation is part in the test bench, not in the test
The mixed signal enabled UVC contains all analyses and cover groups needed to deal with analog signals. The functional coverage is easily shared with the team and gives insight in the verification progress.

## Slide 16: Questions