## Slide 1: Efficient Fault Injection Methods for Safety Software Testing Based on Virtual Prototypes: Application to Powertrain ECU
Dr. Ons Mbarek, Robert Bosch Germany GmbH
Dineshkumar Selvaraj, Infineon Technologies India AG
Romero Chica Jose Miguel, Rajagopal Shenoy, Holger Riethmueller
Robert Bosch Germany GmbH

## Slide 2: Outline
Motivation
Fault Injection Methods: State-of-Art
Challenges of Functional Safety Compliant ECU Platforms
Functional Safety of Powertrain ECU Vs. Virtual Prototyping
Virtual Prototype for MDG1 ECU
Mapping Rules and Fault Injection Methodology
Experimental Results & Observations
Summary

## Slide 3: Motivation
From traditional automotive ICs to ADAS/Autonomous Driving, eMobility, Advanced Security and Connectivity
Risk drivers amplified by growing HW and SW complexity
More than Moore´s Law in Automotive Newcomers
Exida GmbH, FSWG´18

## Slide 4: Motivation
Functional Safety (ISO 26262)
Absence of unacceptable risk due to hazards caused by malfunctioning behavior of E/E systems
Systematic Faults
Random Hardware Faults
Divide and conquer approaches
Early start of HW and SW safety testing and in parallel
ISO 26262 recommends Fault Injection & Simulation
Strong cooperation between OEM and IC suppliers needed

## Slide 5: Motivation
Tier 2 Suppliers
Tier 1 Supplier
OEM Company
ECU Hardware
Functional Architecture
HW Architecture
SW Architecture
System config. description
subsystem
system
ECU Software
RTE
BSW
ECU with SW
CDD
SWC
Safety HW mechanisms
Config.data extract for ECU
SWC description
ECU resource Description
ECU Safety Concept
config. data
Safety SW Librairies
HW Req.
IC Safety Concept
IC Hardware
IC Safety Manual
Assumptions of use
ECU Safety Manual
OEM-Supplier Collaboration

## Slide 6: Fault Injection Methods: State-of-Art
Lack of a standardized methodology for virtual FI
Fault Injection
HW
SW
Simulation Based
Emulation Based
Gate/RTL Simulation
VP Simulation

## Slide 7: Challenges of Functional Safety Compliant ECU Platforms
The E-Gas Monitoring Concept
  Safety concept standardized by the AKEGAS WG
  Applies to powertrain ECU
  Describes the monitoring system structure
  Complies with the ISO 26262 since 2013
  A three-level concept
  L3 relies on two independent components:
    Function Controller (FC)
    Monitoring Module (MM)
HW-dependent

## Slide 8: FuSa of Powertrain ECU Vs. Virtual Prototyping
CDD includes drivers for sensors and ASIC
CDD is project specific with legacy functions
Safety features specifications in AUTOSAR R4.0 onwards.
CDD abides to AUTOSAR interface
Technical Safety Concept Status Report Autosar CP Release 4.3.1

## Slide 9: FuSa of Powertrain ECU Vs. Virtual Prototyping
What/how accurate should we model?
To which extent an unmodified safety SW could be validated on a VP?
Are there any limitations?
I/O
Binary loaded

## Slide 10: Virtual Prototype for MDG1 ECU
VP Use Case Structure
  TLM model of Powertrain Bosch MDG1 ECU
  Infineon AURIXTM 2G MCU model
    32-bit Tricore Fast-Timed Model (FTM) from Synopsys
    Loosely Timed (LT) and Approximately Timed (AT) memory and peripheral IP models
    3 IP suppliers (Synopsys, Bosch and Infineon), one integrator (Infineon)
    Good tradeoff between timing accuracy, functionality accuracy and simulation speed.
  In-house Bosch ASIC & sensor LT models
    External monitoring, low-side and high-side power stages, iginition/injection, power supply …
Powerstage ASICs
Monitoring Module ASIC
Sensor/
Stimuli Generator
SNPS FTM models
IFX AURIXTM 2G Model
Bosch IP/Models

## Slide 11: Virtual Prototype for MDG1 ECU
MDG1 Safety Concept
  Safe system development conform to ISO 26262 up to ASIL-D
  Based on E-Gas concept
  With HW safety mechanisms (SM)
  Possible checks via SW/error-detection HW/combination of both
  AURIXTM 2G MCU saves effort of SW function tests development
    Lockstep cores
    MBIST, LBIST, ECC, etc.

## Slide 12: FI Methodology Flow
A well-structured FI methodology flow:
  For the efficient VP-based FI safety test construction
  Five sequential steps
  Parallel application of the mapping rules

## Slide 13: Mapping Rules
4 mapping rules for the construction of safety test scenarios for VP

## Slide 14: Mapping Rule 1 (MR1)
MR1 applicable during bring-up of a safety SW on a VP
Constraints in VP (e.g. stub functionality) can be overcome via workarounds
Workarounds in form of converters of original SW checks to alternative ones having same validation purpose
Converters intercept at runtime the real software flow and trigger differently the monitoring checks
ADC Monitoring Hardware Design

## Slide 15: Mapping Rule 2 (MR2)
Targets one to one mapping from software test code to a script-based FI scenario
All intermediate steps (error creation, detection and effects checks) are implemented
Preferred when no constraints are observed
PMU Safety Test Case Flow

## Slide 16: Mapping Rule 3 (MR3)
Applicable in case of constraints when applying MR2
Alternatives definition to trigger the fault differently
Inspection of error occurrence flow
Definition of potential entry to inject a fault and get the same effect
No need to perform intermediate behavior of a fault
Consider only obvious parts to the software
Limited possibility of debug and analysis of error path propagation

## Slide 17: Mapping Rule 3 (MR3)
Interconnection SMU, IR, CPU & PMU in AURIXTM 2G
s
Set the LMU Safety control register to inject ECC
 non-modeled error injection registers in VP
Set the LMU control register for hardware detection logic of the ECC
 non-modeled HW provided error detection logic
s
Trigger the SMU input alarm

## Slide 18: Mapping Rule 4 (MR4)
Creation of new fault scenarios hard to apply on real HW
Increases test coverage
Examples: short circuit, open load, over-and under voltage,
Shut-off path test (E-Gas L3)
Shut-off Path and Query-Response Monitoring Concept

## Slide 19: No Mapping Rule
Software tests cannot be converted to VP-based ones
Nor new pure VP scenarios can be imagined
Caused by limitations in a VP:
  Non-modeled/Stub functionality in VP
  Not enough accurate offered by VP

## Slide 20: Methodology for VP-based FI Tests Construction
Step 1: Analysis of Safety Requirements Test Cases
  Analysis of software test case
  Understanding of software behavior leading to safety error reaction
  Identification of triggering events/timing points
  Choice of mapping rule based on examined offered mechanisms in VP Vs. SW safety requirements.

## Slide 21: Methodology for VP-based FI Tests Construction
Step 2: Definition of Fault Library
  Definition of FI inspectors library
  FI inspectors are responsible to monitor execution/triggering events and inject faults into target modules.

## Slide 22: Methodology for VP-based FI Tests Construction
Step 3: Definition of Fault Method Library
  Definition of callbacks to be executed at event occurrences
  Callbacks inject faults at desired timing points
  Consider latency, side effects and atomicity

## Slide 23: Methodology for VP-based FI Tests Construction
Step 4: Definition of Fault Scenario Sequences
  Specification of test scenario flow starting from a triggering condition until calling re-defined callbacks in the right sequential order

## Slide 24: Methodology for VP-based FI Tests Construction
Step 5: Definition of Recovery from Error States Library
  Definition of checks library for desired safety reaction validation
  Check error path propagation in dependent layers

## Slide 25: Experimental Results & Observations
Main Benefits:
  Early basic checks of safety monitoring software 6 Months before real silicon
  Better management of delays in silicon shipping
  Up to 40% of critical L3 software reactions tested on VP
  Testing of up to 6 critical safety error scenarios hard to realize ona real ECU thanks to VP flexibility.
  Quick production software bring-up, free of traps and uncomprehensive shut-down and resets
  High quality, on-time and safe software releases to OEM

## Slide 26: Experimental Results & Observations
Limitations and Main Conclusions:
  Not able to apply the 60% test cases due to missing functional behavior in MCU model
  Additional effort and cost will be involved if VP is not already part of SoC Product Life Cycle for pre-silicon SW development
  Tools and models cannot be trusted due to lack of ISO 26262 qualification
  Presented approach could ONLY be considered as efficiency measure
  Software tests have to run in the end on the real silicon

## Slide 27: Summary
Proof of Feasibility:
  A well-structured FI methodology with proved benefits on real automotive project
  VP could ONLY help in a safe critical product design ecosystem
Lessons Learnt & Call for Actions:
  Abording FuSA late in ECU product development phase is not an option!
  Serious consideration of ISO 26262 qualification by VP suppliers
  Needs of safety architecture exploration for the next generations of ECU
  Needs of strong cooperation between VP tool and model vendors to promote usefulness of VP for safety SW testing
Future Works:
  Leveraging the approach in post-silicon phase via automated test setup

## Slide 28: Questions