## Slide 1: Hardware construction with SystemC
Roman Popov ( Intel Corporation)
Moiseev Mikhail (Intel Corporation)

## Slide 2: Introduction
Hardware construction (HC) – algorithmic generation of HW structure using high-level language
  Good for highly parameterizable designs, regular structure
  Popularized recently by Chisel (Scala-based HDL)
SystemC – C++-based modeling language
  Can be synthesized with HLS (High-level synthesis)
Can we use SystemC for HC? What is missing in library and tools?
Design domain | Conventional design technique | Emerging “ESL” approach
Structural | Manual module instantiation and wiring | Hardware construction
Behavioral | RTL (Cycle-accurate) process specification | High-level synthesis

## Slide 3: Design generation in SystemC
Highly-reusable building blocks can be created with C++ templates
Hardware structure is generated during elaboration phase of model execution
  Arbitrary C++ can be applied
So, SystemC is a hardware construction language, but:
  Modern HLS tool support for elaboration-time programming is minimal
  Good design methodology required (how to design for reuse?)

## Slide 4: Example problem 1: Synchronous modules
struct dut : sc_module { sc_in<bool> clk{"clk"}; sc_in<bool> arst_n{"arst_n"}; p2p_get_init<int> din{"din"}; p2p_put_init<int> dout{"dout"}; SC_CTOR (dut) { SC_THREAD(dut_process); sensitive << clk.pos(); reset_signal_is(arst_n, false); din.clk(clk); din.arst_n(arst_n); dout.clk(clk); dout.arst_n(arst_n); } void dut_process() {
// YOUR TOP SECRET IP
}
};
struct dut : sync_module {
p2p_get_init<int> din{"din"}; p2p_put_init<int> dout{"dout"}; SC_CTOR (dut) {
SYNC_CTHREAD(dut_process);
} void dut_process() {
// YOUR TOP SECRET IP
}
};

## Slide 5: Synchronous modules implementation
struct sync_module : sc_module { sc_in<bool> clk{"clk"}; sc_in<bool> arst_n{"arst_n"};
void before_end_of_elaboration() override
{
for( auto* child : get_child_objects()) { if (sync_module *sync_child = dynamic_cast<sync_module *>(child)) { sync_child->clock(clock); sync_child->async_reset_n(async_reset_n); } }
} };

## Slide 6: Example problem 2: SoC interconnect generation
Reusable interconnect generator:
  Configurable number of master and slave devices, address space, QoS policies, multiple protocols support, multiple clock domains…
Today:
Create a library of building blocks
Connect them manually based on architecture requirements
In future:
Connect them algorithmically based on requirements
What would be a good API for such generator?
  Variadic template ?
  template<typename … DeviceTraitsT>

## Slide 7: Simple solution: Creational design patterns
SoCFabricBuilder fabBuilder;
fabBuilder.addAXIMaster(device0, device0Params, ... );
...
fabBuilder.addAHBSlave(deviceN, deviceNParams, ...);
fabBuilder.setArchitecture(NoC);
// Validate requirements
// Generate interconnect by instantiating building block
// Connect devices
socFabric = fabBuilder.generate();

## Slide 8: Impact on synthesizable subset
Today: SystemC Synthesizable subset does not clearly distinguish elaboration and simulation phases
In future: any C++ should be allowed during elaboration, without restrictions
struct HLSModule : sc_module {
SC_CTOR(HLSModule) {
// Arbitary C++ is allowed: STL, File I/O, whatever else
SC_CTHREAD(hls_cthread, clk.pos());
}
// OK. Discarded if not referenced from process
std::unordered_map<...> elabOnlyMap;
void hls_cthread() {
// Limited C++ support with restrictions implied by Syn Subset
}
HC
HLS
HC - HLS
interface

## Slide 9: Elaboration-time defined constant semantics
During elaboration a constant value or constant-sized array can be created
Types to express this notion will be required
// sc_vector - elaboration-time sized array of sc_objects
sc_vector<device> devices{“devices”};
devices.init(10); // instantiate 10 devices
// Cannot be resized during simulation
// Bitwidth of signal defined during elaboration
sc_signal<sc_unsigned> fifo_write_ptr;

## Slide 10: Implementation options
Option 1: Static analysis of source code, interpretation of module constructor
  Utilized by commercial HLS tools
  Problem: library dependencies (standard library, SystemC itself)
  Why interpret C++ if we can compile and run it?
Option 2: Run model, stop on start_of_simulation(); Extract module structure from memory.
  Problem: C++ has no runtime reflection API

## Slide 11: Sources of reflection metadata
On Linux, C++ has standardized Application Binary Interface, Itanium ABI. Supported both by GCC and Clang
  Specifies layout of all types in memory
Sources of information about types:
  Compiler intermediate representations
    Examples: Clang AST, LLVM IR
  Debug information
    Examples: DWARF
Already utilized by some SystemC front-ends: Pinapa, PinaVM
  And in commercial SystemC debuggers

## Slide 12: Our experience
Implemented a GDB-based SystemC elaboration
  2 man-months of development
  Works perfectly on our existing SystemC designs
Generates a Verilog netlist (without process bodies)
Arbitrary C++ is allowed
  Including non-standard SystemC
Experimenting with applications

## Slide 13: Elaboration algorithm
struct bottom: sc_module {
sc_in<int> in{"in"};
};
struct top : sc_module {
sc_signal<int> sig{"sig"};
bottom b{"b"};
SC_CTOR(top) {
b.in(sig);
}
};
Obj ID | ADDR | Type
0 (top) | 0x0 | top
1 (sig) | 0x0 | sc_signal<int>
2 (b) | 0x10 | bottom
3 (b.in) | 0x10 | sc_in<int>
Algorithm (two passes):
Traverse design hierarchy to build design tree and typed memory map
For each pointer find its pointee in memory map based on pointer value (stored address) and pointer type
  For polymorphic objects (for example sc_objects) use dynamic type from RTTI

## Slide 14: Dynamic allocation
int * dangling;
int * arrayp = new int[10];
Information about dynamic allocations is lost
Solutions
  Tracing new operator
template<class T, class... Args>
T* sc_new(Args&&... args) // saves info inside host module
  For sc_objects use SystemC built-in design-tree introspection (sc_object::get_child_objects )
In our legacy code: all dynamic allocation were sc_objects, no code modification required

## Slide 15: Conclusions
SystemC has a potential to become powerful HC language
Combination of compile-time and elaboration-time programming is both challenge and opportunity
  Good design methodology required
Separation of elaboration and simulation phases required in synthesizable subset
  Arbitrary C++ can be allowed for elaboration
Reflection-based dynamic elaboration is a simple path for tool implementation

## Slide 16: Questions