## Slide 1: Using UVM-ML library to enable reuse of TLM2.0 models in UVM test benches
Sarmad Dahir (sarmad@cadence.com)
Cadence Design Systems
DVCON Europe 2018

## Slide 2: Hardware Design and Verification Challenges

## Slide 3: Growing Verification Challenges
As HW design complexity is increasing, the verification part of the ASIC development flow is also becoming ever more challenging and important.
Advanced verification methodologies like metric-driven verification are used to address these challenges
  ASIC verifiers rely on using UVCs and reference models, from different sources, to build their verification environments.
  Both Loosely-Timed TLM 2.0 models as well as UVM make use of sockets/ports, but they cannot be directly connected to each other, which adds a limitation on the reusability of the reference models.
  To overcome the above limitation, verifiers need to manually implement an additional ad-hoc wrapper layer that enables the communication between TLM and UVM, e.g. by using DPI-C.
  A more generic solution is to use a library, like UVM-ML, that enables direct communication between different frameworks.
Notes: Nowadays, a lot of the data processing algorithms are implemented in specialized hardware instead of software

## Slide 4: TLM 2.0 Models and UVM Multi-Language Library
The hardware design flow usually starts with an early virtual prototypes development phase where reference models are developed to explore different aspects of the target algorithms, e.g. performance, accuracy and architecture complexity.
  These virtual prototypes are in some cases made available before the hardware design phase starts and are used as early software development platforms.
TLM 2.0 models are a natural fit to use with UVM testbenches because both UVM, as well as TLM and SystemC®, make use of sockets, ports, etc. and abstract data representation.
To leverage all available types of UVCs and HW reference models in verification testbenches users need to have a flexible and easy to use environment where these different components can co-exist and work seamlessly together.
By using UVM ML, verifiers can reuse the TLM 2.0 models in their verification environments by directly connecting the ports of the testbench to the ports of the TLM model.
Notes: Use right language/technology to solve right problem. Ref models are in C++ or TLM. Verification TB is in UVM-SV or UVM-e
Using UVM-ML we can overcome the limitations when connecting different frameworks in ML environments

## Slide 5: Introduction to UVM Multi-Language

## Slide 6: UVM Multi-Language Development
The UVM Multi-Language library was developed by a collaboration between Cadence and AMD
The people and the library were the base for the Accellera UVM-ML Open Architecture (OA) working group
UVM-ML library is available as open source (since July 2012)
  http://forums.accellera.org/files/file/65-uvm-ml-open-architecture
  And it’s also provided within Cadence® Xcelium™ installations

## Slide 7: UVM-ML OA Architecture
Top2
Framework 2
ML-Adapter
Framework 1
Top1
vip1
vip2
ML-Adapter
Framework 3
Top3
Top4
Services
ML-Adapter
Service FW
Services
Service FW
Services
Service FW n
Services
ML-Adapter
ML-Adapter
ML-Adapter
UVM-ML Backplane
Provided API
Required API
Service API
Framework / Routing / Proxy Info
Registration API
Backplane serves as a central hub connecting the frameworks in a star topology (not peer-to-peer)
Each framework is connected via an adapter to the backplane using the same API
System services may be provided by frameworks or as dedicated services
Notes: On this diagram, Framework 1 can be, for example, UVM SystemVerilog, Framework 2 - UVM e, Framework 3- SystemC etc.
Different frameworks can be deployed in the same language (for example, UVM and VMM are both in SystemVerilog).
The backplane serves as a hub between two or more integrated frameworks and holds information about the overall topology, which is necessary for routing.
Each framework is connected via an adapter to the backplane using the same API.
Any number of frameworks can be interconnected at the same time.
The overall UVM-ML OA architecture enables collaboration between the frameworks while abstracting away from specific methodologies and languages.
system services: The backplane is used for broadcasting messages from a service provider to the rest of the frameworks (for example, the phasing service is implemented in this way).

## Slide 8: UVM-ML OA Key Features
Modular and extensible architecture
Framework and simulator independent API
TLM communication (TLM1 and TLM2)
Coordinated initialization/bring-up of all participating libraries
Phase synchronization
Unified hierarchy solution: Hierarchical construction of a multi-language verification environment
Multi-language configuration
Multi-language sequence layering
Multi-language debugging/synchronization
Backplane
FW
2
FW
1
FW
n
Frameworks
…
VC
(e)
VC
(e)
VC
(sc)
VC
(sv)
VC
(e)
Notes: other frameworks can be added by users – anyone who wants to add a framework, implement the adapter for it. E.g. – one customer implemented adapter for OVM.

## Slide 9: Synchronized Phases
Coordinate phases between the various frameworks
Ensures that components are configured then created, ports created then connected, etc.
A
B
C
Framework 1
(e.g., UVM-SV)
Framework 2
(e.g., UVM-SC)
Framework 3
(e.g., UVM-e)
pre-generate, post-generate
build
end_of_elaboration
start_test
connect_pointers, connect_ports
connect
start_of_simulation
run
end_of_construction
end_of_elaboration
start_of_simulation

## Slide 10: Example of Using UVM-ML in a UVM+TLM Testbench

## Slide 11: Topology of Verification TB when reusing the TLM Model
TB_TOP
ENV
TEST
Scoreboard
Virt Sequencer
Virt Sequence
i_dut_0
i_dut_1
TLM Adapter
Agent B
seqr
driver
mon
Agent A
driver
seqr
mon
i_dut_0
i_dut_1
UVM-ML
UVM TB
RTL DUT
TLM Model
Notes: Blue is the UVM TB, yellow is DUT, green is TLM ref model
TLM is now a component under the TB (unified hierarchy approach)
Sockets between UVM and TLM are connected using UVM_ML.

## Slide 12: Comparing HDL vs TLM in the Verification Testbench
The UVC monitor passes the observed transactions to the TLM adapter.
The TLM adapter maps UVM sequence items to TLM GP and sends them, over UVM-ML, to the TLM model.
The response from TLM is passed to the scoreboard through the TLM adapter.
This way the testbench scoreboard can compare the functionality of RTL to the TLM reference model.
TB_TOP
ENV
TEST
Scoreboard
Virt Sequencer
Virt Sequence
i_dut_0
i_dut_1
TLM Adapter
Agent B
seqr
driver
mon
Agent A
driver
seqr
mon
i_dut_0
i_dut_1
UVM-ML

## Slide 13: Unified Hierarchy – Instantiating a SystemC Component Under UVM-SV Component
Each type must be defined in the respective language
In the SV component:
  Define a member of type child_component_proxy (or uvm_component, which it inherits)
  Create it using child_component_proxy uvm_ml::uvm_ml_create_component()
class myenv extends uvm_env;
uvm_component tlm_wrapper_inst;
function void build_phase(uvm_phase phase);
…
tlm_wrapper_inst = uvm_ml_create_component("SC",
"top_wrapper",
"tlm_wrapper_inst",
this);
endfunction
…
SV
Foreign Type
Instance Name
Parent
class top_wrapper : public uvm_component {}
SC

## Slide 14: UVM-ML Integration Step by Step

## Slide 15: Importing the UVM-ML Library
In addition to the RTL and testbench, users need to load/compile the backplane + adapters in order to use UVM-ML features
In SystemVerilog:
import uvm_pkg::*;
`include "uvm_macros.svh"
import uvm_ml::*;
In SystemC®:
#include "uvm_ml.h"
#include "ml_tlm2.h"
Notes: The SV Adapter is a SV package (uvm_ml) (compiled as part of SV compilation) and DPI C source files compiled into a shared library.
The Backplane is written in C++ but communicates in C

## Slide 16: Running the Test Under UVM-ML
When incorporating UVM-ML in your environment, you need to let UVM-ML take control over building your UVM environment and running its phases
Instead of using the regular UVM “run_test()” method, use the UVM-ML variant “uvm_ml_run_test(string)”:
string tops[1];
initial begin
…
tops[0] = "";
uvm_ml_run_test(tops);
…
The test name can still be passed using the plus argument +UVM_TESTNAME to the xrun command

## Slide 17: Socket Registration on SV Side
Using UVM-ML “register” API, TLM sockets are registered for connection to SC domain.
UVM-ML Registration:
function void phase_ended(uvm_phase phase);
if (phase.get_name() == "build") begin
uvm_ml::ml_tlm2#()::register(initiator_socket_0);
uvm_ml::ml_tlm2#()::register(initiator_socket_1);
end
endfunction
The registration should be done at phases_ended() of build phase as shown above

## Slide 18: Socket Registration on SystemC Side
The sockets registration needs to be done in SystemC® side also, which can be done by using the socket registration macros:
void build() {
full_target_socket_name_0 = ML_TLM2_REGISTER_TARGET(dut_inst, tlm_generic_payload, reg_in_0, 32);
full_target_socket_name_1 = ML_TLM2_REGISTER_TARGET(dut_inst, tlm_generic_payload, reg_in_1, 32);
}
Notes:
The macros above return a string value, which actually is the hierarchical path to the socket after elaboration
  this can be printed out for debugging
Instead of using the macros, you can also call the socket registration functions directly in order to take advantage of all additional arguments provided: ml_tlm2_register_initiator <tlm_generic_payload, 32>(top_inst.dut_i, top_inst.dut_i.o_port[0], "o_port_0");

## Slide 19: Socket Connection
The connection from SV to SystemC ® domain can be done in either the SV or SystemC ® side; here it is done in SV side in the connect_phase() function:
function void connect_phase(uvm_phase phase);
void'(uvm_ml::connect(initiator_socket_0.get_full_name(), "uvm_test_top.tb_env.tlm_wrapper_inst.dut_inst.reg_in_0"));
void'(uvm_ml::connect(initiator_socket_1.get_full_name(), "uvm_test_top.tb_env.tlm_wrapper_inst.dut_inst.reg_in_1"));
endfunction
The SystemC target sockets names could be extracted either by looking into the topology of the testbench or using the return value of SystemC socket registration as was discussed in previous slide

## Slide 20: Using TLM Generic Payload Extensions with UVM-ML

## Slide 21: Generic Payload Extension Updates on SystemVerilog Side
The class that defines the GP extension fields must use the UVM filed registration macros which define the packer and unpacker functions under-the-hood; these functions are used by UVM-ML library for serialization and de-serialization of GP for transporting and collecting data:
`uvm_object_utils_begin(vip_transfer_gp_ext)
`uvm_field_int(m_id, UVM_ALL_ON)
`uvm_object_utils_end
Also, the names of the GP extension classes in SV and SystemC® side should match; if they don’t, then specify the matches using the set_type_match() function:
if(!uvm_ml::set_type_match("sv:vip_transfer_gp_ext","sc:transfer_gp_ext"))
`uvm_fatal(get_name(), "Cannot match the GP extension types.")
The above function call tells UVM-ML that the SV class “vip_transfer_gp_ext”, which is the class that specifies the GP extension, should be considered the corresponding match for the SC class “transfer_gp_ext”

## Slide 22: Generic Payload Extension Updates on SystemC Side
The field registration macros are needed in SystemC® side too; on the SystemC side, they are out-of-class macros. This enables code reuse as these macros can be added in a top TB file only when used in a TB that needs to send this class type across different frameworks:
ML_TLM2_GP_EXT_BEGIN(transfer_gp_ext)
ML_TLM2_FIELD_ACCESSORS(uint32_t, get_id, set_id)
ML_TLM2_GP_EXT_END(transfer_gp_ext)
Notes:
Here we used the “ACCESSORS” macro that uses the get_id()/set_id() member functions of the GP extension class to access the data field, which is because the data members are declared private; if they were public then we could use the macro “ML_TLM2_FIELD” that takes the data member as argument
The order of field registration macros should match in both SV and SystemC sides for the data to be unpacked properly

## Slide 23: Using the Generic Payload Extension on SystemVerilog & SystemC
Using the GP extensions is done as per regular TLM flow; no UVM-ML specific APIs are required
In both UVM-SV and SystemC®, use the set_extension() and get_extension() functions to add/get the GP-extension object to/from the GP

## Slide 24: UVM-ML Integration Debugging Helpers
You can add the following function to call in your SC code before any socket registration, to get the list of registered sockets in both SystemC and SV: void(uvm_ml_execute_command("uvm_ml_trace_register -on"));
You can also get the list of registered sockets by using this Xcelium™ TCL command: uvm_ml trace_register_tlm
To stop the simulation at the end of the connect phase and print the connections to make sure they’ve been done properly, use the following Xcelium™ TCL commands: uvm_ml_phase -stop_at -end connect run uvm_ml_print_connections
The following TCL command shows the types being matched between the different frameworks: uvm_ml print_type_match

## Slide 25: Discussion and summary

## Slide 26: Exploring alternative solutions to UVM-ML
We also implemented a version of the TB that uses DPI-C calls, instead of using UVM-ML library, to communicate between UVM-SV and SystemC domains.
Simulation time and memory usage were slightly lower in this version but the code complexity was significantly higher.
  The code had to include ad-hoc pieces that limit code re-usability.
  Missing UVM-ML features such as auto conversion of class types, list registered/connected sockets, phase synchronization, etc.
TB_TOP
ENV
TEST
Scoreboard
+ ad-hoc DPI-C
Virt Sequencer
Virt Sequence
i_dut_0
i_dut_1
Agent B
seqr
driver
mon
Agent A
driver
seqr
mon
UVM TB
RTL DUT
TLM Model
sc_main
TLM top
+ ad-hoc DPI
i_dut_0
i_dut_1
write_rtl2tlm(...)
Notes: We are limited to DPI-C capabilities, such as: DPI can handle conversion of basic data types between SystemVerilog and SystemC but, unlike UVM-ML, it cannot handle auto conversion of class objects
No unified hierarchy support.
Ad-hoc code in both SV and SC sides.
Call from SV to global function need to modify the SC code to give this specific function access to the sockets.

## Slide 27: Summary
UVM-ML is an easy and straight forward approach to integrate and connect TLM models into a MDV environment.
  The complexity of the UVM scoreboard component was significantly lower as we didn’t need to re-model the intended DUT functionality to support the self-checking test bench approach.
  Reduced TB development time by leveraging on code reuse.
  The reduction of the test bench complexity did not cause any decrease in verification quality .
  It offers advanced and convenient features like unified hierarchy and phase synchronization.
Allows direct connection of TLM models and UVM test benches by reusing already existing sockets, ports.
Open source library which is simulator independent.
  Can be downloaded from Accellera and is also delivered with Xcelium™ simulator.
Cadence UVM-ML support team is ready to help if needed:
  support_uvm_ml@cadence.com

## Slide 29: More info can also be found here
ISBN-13: 978-1105113758
ISBN-10: 1105113752

## Slide 30: xrun Options for Building UVM-ML Testbenches
-f $XCELIUM_INST_DIR/tools/methodology/UVM/CDNS-1.2-ML/ml/run_utils/ml_options.32.f
-ml_uvm
-uvmhome CDNS-1.2-ML
-f $XCELIUM_INST_DIR/tools/methodology/UVM/CDNS-1.2-ML/ml/run_utils/sc_options.32.f
-sysc
-DSC_INCLUDE_DYNAMIC_PROCESSES
-f $XCELIUM_INST_DIR/tools/methodology/UVM/CDNS-1.2-ML/ml/run_utils/sv_1.2_options.32.f
-sv_lib /proj/asic/tools/cadence/xcelium/XCELIUM_17.04.013/tools/methodology/UVM/CDNS-1.2-ML/ml/lib/libuvm_sv_ml.so
+UVM_NO_RELNOTES
-nocopyright